## Slide 1
Advances in Driving Research: Models, Data, and New Methods
Paul Green, Heejin Jeong, Brian Lin, Te-Ping Kang – U. of Michigan (www.umich.edu/~driving)
How should driver decision making at intersections be modeled?
How do the traffic signal phase (green, yellow, red), the time from an intersection when the signal changes, what other vehicles are doing (turning), driver age and gender, and other factors affect driving through intersections? -> Examine: speed, acceleration, jerk, and throttle histories
In 2 experiments so far (24 subjects/experiment), subjects drove through 2 sets of 70 intersections following a lead vehicle (and being followed). At each intersection, the signal was either green, yellow (3 time options), or red. For the yellow signals, vehicles at the intersection could be (1) stationary, (2) intrude into the intersection, or (3) turn in front of them unexpectedly as shown in the figure below. In experiment 2, augmented reality warnings were provided.
Until now, there were no agreed upon definitions for most driving performance measures and statistics, so studies were often not replicable. SAE Recommended Practice J2944, with which journals & conferences will require compliance, (or papers will be rejected) defines them.
2. Very low-cost eye-fixation systems (1 - 10% price of lab system) can be good enough.
3. For educational and demonstration purposes, a free, open source driving simulator (OpenDS) + specially modified (ask how) Logitech G27 driving game unit ($250) can be used instead of research simulators.
Models and Data on Driving Through Intersections
New Methods
Gazepoint ($500 w/ SDK)
Accuracy: 1 deg claimed (actually better than Eyetribe)
45 to 75 cm depth
real time visualization
preferred over Eyetribe
Eyetribe ($100 w/ SDK)
Accuracy: 1 deg claimed
+/- 15 cm depth
3 systems @ AutoUI workshop
Keeping simulator hardware at the library as “reserve books” students can borrow overcomes many problems and supports class use.
Cost is no longer a barrier for the “have nots” wanting to do simulator research
CPS Synergy: Collaborative Research:
Formal Design of Semi-autonomous Cyber Physical Transportation Systems
PI: Domitilla Del Vecchio (MIT)
Co-PIs: Paul Green ( U. of Michigan),
Emilio Frazzoli (MIT)
NSF award 1239182
How can augmented reality be used to present warnings?
For most terms, there is a base concept (e.g., Time to Collision) and multiple variations (Minumum, Adjusted Minimum, Inverse, etc.)
Some examples and the number of variations of the term include:
Response Time (15)
Time to Collision (2)
Lateral Lane Position (3)
Std Dev. of Lane Position (3)
Yes, there really are 11 ways to define a lane departure.
Lane Departure (11)
Time to Line Crossing (3)
Lane Change (5)
Roadway Departure (3)
4. Having the following vehicle honk when the subject drives too slowly leads to more realistic speeds.
For realistic behavior, one needs rules for starting, maintaining speed, and approaching intersections. What else would you suggest matters?
original
G27
modified G27
9 point,
3 screen
calibration
real vehicle:
2013 Buick
Encore
Extensive data have been collected . See the Del Vecchio: MIT poster.
Teasers are below.
But doing good research also requires knowing how to use the equipment.
Notes: 9 pt
3 screen
calibration