## Slide 1
CPS: Synergy: Thermal-Aware Management of Cyber-Physical Systems
K.G. Shin; E.M. Atkins
University of Michigan
C.M. Krishna; I. Koren
University of Massachusetts
S. Wang
General Motors
Cyber-physical processors work in harsh environments and often suffer very high operating temperatures.
High temperature can accelerate processor aging and increase failure rate.
Effective thermal-aware management is required to meet
the computational demands of the application while reducing processor thermal stress.
Motivation
Failure Sources
Electromigration
Dielectric breakdown
Negative bias temperature instability
All strongly dependent on temperature
Our Approach
Controlled Plant:
Current state
Dynamics
Desired trajectory
Safety envelope
Dynamic computational workload and core assignment
Core reconfiguration
Balance quality of control against thermal stress
Online Thermal Management
System-Wide Manager
Periodically sample core subunit temps; estimate core reliability
If est. core reliability differential exceeds a given threshold, migrate tasks away from the less reliable core.
Core-Level Manager
Adjust core speeds
Power gating
Architecture adaptation
System Provisioning
Optimization & Validation
Unmanned Aerial Vehicles (UAVs)
Optimize UAV mission cost J over time, energy use, information (entropy), & temperature (y)
  Design variables: physical (p) UAV speed v(t) and onboard core (c) use r(t)
Lab & wind tunnel experiments: validate temperature dynamics models
Steady State Temperature
over UAV Engine (Airspeed)
& Core (Cyber) Controls
Pareto Fronts over Temperature, Energy,
Entropy (Info.), & Time
,