## Slide 1: CPS and the Mobile Tsunami
Hari Balakrishnan
M.I.T. cartel.csail.mit.edu

## Slide 2: Road Transportation Challenges
Accidents & hazards Congestion
Degrading roads Pollution
80% of world’s population is in places where automobile growth is occurring at >20% per year

## Slide 3: CarTel: Vehicular CPS with Mobile Sensing
Servers
Smartphones or embedded device in vehicles
Highly granular raw data collection
Aggregation provides environmental info
Details enable personalized service
Modeling, prediction, analysis
Location-based vehicular apps
Protect user location privacy
CITA distrib. prog. framework
V2V mobile mesh
V2I
Trajectory & delay estimation (VTrack, CTrack)
Traffic-aware stochastic routing
Usage-based tolling
Road surface & hazard monitoring (Pothole Patrol)
Driver safety scoring & insurance
Partners: PlanetTran, Ford, Insurance Co.
Notes: V2I == Vehicle-to-Infrastructure
V2V = Vehicle-to-Vehicle

## Slide 4: Why Smartphones for CPS?
Chart: 
| X | Y | Z
 | 215000 | 490000 | 1700000
Per day, in Q2 2012
Births-deaths
Births
Smartphones
Truly ubiquitous!

## Slide 5: Why Smartphones for CPS?
GPS
WiFi
Cell
Accl
Gyro
Compass
Mic
Light
Proximity
Barometer
Detailed driving activity
Mileage Road types
Hours
Delays & congestion
Speed profiles
Accel events
Hazards

## Slide 6: Smartphones Key to Mass Adoption
Telematics Update says (2012):
  Smartphones may emerge as a way to incentivize the insurance telematics model.
  Connecting insurance telematics solutions to smartphones can provide transparency to drivers and a degree of control.

## Slide 7: Challenges
Clean models from noisy data
Distributed programming framework
Privacy and security protocols
Actuation & feedback

## Slide 8: Noisy Data
Chart: 
| GPS-1 | GPS-180 | NetLoc
 | 9.8 | 46 | 56
Hours
3-axis accel
Accurate probabilistic models from inherently noisy data, gathered in a battery-efficient way
Cellular/WiFi locations
Notes: Phone not oriented in fixed position, user can pick up the phone, reorient, etc.
Gravity vector changes depending on hills and orientation
Sensor has drift, sensitive to temperature changes

## Slide 9: Accurate Models from Noisy Data
HMM RF fingerprints to grid sequence
HMM smooth grid to map
Raw points
Smooth + interpolate grid sequence
VTrack, SenSys 2009
CTrack, NSDI 2011
Notes: I haven’t shown the grid lines here, they are kind of hard to see. Overlay grid on to second picture.

## Slide 10: Pothole Patrol (P2)
Road infrastructure degrading rapidly
Over 500K pothole-related insurance claims/year
Thousands of damage claims per year against states
Not enough money to fix every problem
J. Eriksson, L. Girod, B. Hull, R. Newton, S. Madden, HB, Mobisys 2008

## Slide 11
Notes: potholes annoying, scary?
significant costs to cities, car owners
‘report a pothole’ programs
even lawsuits

## Slide 12: Code In The Air Distributed Tasking & Coordination
GPS
WiFi
Cell
Accl
Gyro
Compass
Mic
Light
Proximity
Walking
Running
Sitting
Biking
Driving
Indoors
Outdoors
AtHome
AtOffice
Barometer
CITA lowers the barrier for programming and executing distributed tasking applications

## Slide 13: CITA Supports Tasking & Coordination
Background service runs continuously, captures sensor data
Apps: server-side scripts only, using activity as primitive (no sensing code)
Trigger actions when right conditions are met
End-user programming on mobile
Support coordination between multiple users or devices

## Slide 14: Changing User Behavior with Smarter Tolling & Insurance Models
Imagine a system with (almost) no road-side tolling infrastructure
Software on mobile device monitors location tracks
Device and server run protocol to compute payment or rebate
Device (user) does not trust server with location tracks
Server does not trust device (tampering)
Account ID
Antenna

## Slide 15: Applications
Usage-based tolls
Speeding tickets
  Did the driver ever travel faster than 70 mph?
Usage-based insurance
  How many miles this month did the driver travel on freeways?
  How many “hard braking” events?
Notes: We looked at several different applications.;
This being the general protocol., we discuss four specific Say that our extensive example is the road pricing example
As one application we show how to compute times over speed limit

## Slide 16: VPriv: Enabling Private Aggregates
Calculations for tolling, insurance, and violations are functions over time-location tuples
Compute such functions privately in zero-knowledge
VPriv designed from scratch; cryptographic commitment protocol w/ homomorphic encryption
Applicable to sum of cost functions
Efficient – 10000x faster than generalized reductions
R. Popa, HB, A. Blumberg, Usenix Security, 2009
R. Popa, HB, A. Blumberg, ACM CCS, 2011

## Slide 17: Summary
Vehicular CPS should embrace mobile smartphones and use that as a “hub”
Real-time vehicular control
V2V comm.
V2I: traffic,
navigation,
incidents
In-car driver feedback
Driver reports
Safety analysis
Tolling
Usage-based insurance rebates
Fixing roads
… building new roads
Time
milli seconds
weeks- months
multiple seconds
minutes
days