## Slide 1
Abstraction of Cyber-Physical Interplays and Its Application to CPS Design
Adaptive Fault-Tolerance
Motivation: Traditional massive redundancy is wasteful when used irrespective of controlled plant state. Adapting redundancy level to current plant state is much more efficient.
Approach: Subdivide plant allowed state-space according to how much fault-tolerance is needed.
  S1: No FT required
  S2: Fail-stop sufficient (e.g., duplex)
  S3: Full fault-masking required (e.g., triplex)
Benefits: Reduces processor utilization, which decreases energy consumption as well as thermal stress thus improving reliability.
Core Philosophy
Computer response time has significance in both control and computational domains
  Control Domain: Manifests itself as feedback delay; its effect is to degrade quality of control. Extent of degradation depends on current controlled plant state.
  Computational Domain: Affected by scheduling algorithms and the total computational workload.
Impact of response time and computational correctness can be quantified as a function of current controlled plant state. Cost functions can be derived by analyzing controlled plant dynamics.
CPS Co-Regulation
Proactive Fault Tolerance Tool
Continuous-State Feedback Control
  Coupled linear system with physical & control task execution states & actuators
  Spacecraft attitude control application
CPS Co-Optimization
  Multi-objective optimization over cyber and physical costs including actuation energy, time, processing load, and information entropy
  Unmanned Aircraft System (UAS) application:
Co-Optimization: Pareto Front over Total Energy, Time, and Information Entropy Costs for a UAS Surveillance Mission
Controlled Plant State
Control Algorithm Repertoire
Task Cost Functions, Periods, Deadlines
Control Algorithm Selection, Rate
Cyber system state and computation progress
F.T. Task Scheduler
Processor Architecture Configuration
Energy Resources Manager
Cyber-physical
Feedback Control
Cost as a function of Aircraft Velocity (Speed) and Computational (Cyber) Rate; Information Gain is a function of Cyber Rate