## Slide 1
NSF CNS-1035340
Architecture and Distributed Management for Reliable Mega-scale Smart Grids
P. R. Kumar, Texas A&M University
Wind Power and Cloud Computing
1
Diversity of Wind Power
2
Send Workload to Where Wind is Available
3
4
Key Contributions
5
Trace-based Simulation
6
WPA Algorithm vs. Naive Load Balance
7
How Many Data Centers Are Needed
8
Correlation Coefficient vs. Coefficient of Variation
9
The Case of Three Data Centers
9
The Answer Is Blowing in the Wind: Powering Data Centers with Wind Energy
P. R. Kumar
With
Yan Gao, Zheng Zeng and Xue Liu
Wind power:
Uncontrollable
Unpredictable
Wind power is inefficiently used
Internet
Data Center
Data Center
Data Center
Energy consumption causes
significant environmental issue
Diversity of supply from many indep. sources
Idea: when wind power is not available in A, B could have wind power
  Assigning work to B prevents A from using power from grid
Requirement: A and B are not well correlated
+
Stable Envelope
=
Internet
Data Center
Data Center
Data Center
Benefits:
Wind energy can be better utilized
GHG emission of Cloud is reduced
Is it feasible to achieve “entirely green”
Cloud Computing services?
Present a novel architecture for wind powered IDCs
Provide an efficient Wind-power Aware (WPA) workload mapping algorithm
Find that building only a small number of data centers can obtain most of the improvement
Show that the appropriate wind farm selection plays important role in achieving high wind-power utilization
Propose to use coefficient of variation as metric for wind farm selection
Real-world traces for both wind power and workloads
Power consumption is proportional to the workload in the data center
A threshold for the maximum number of jobs that a server can accommodate is set so that QoS is guaranteed
A central workload dispatcher that maps client requests to data centers
WPA tracks the ratio of power consumption to the effective wind power
WPA routes each request to the data center with the minimum ratio
Chart: 
| WPA | Naive
datacenter1 | 0.2 | 0.24
datacenter2 | 0.05 | 0.01
datacenter3 | 0.05 | 0.02
Chart: 
| WPA | Naive
Brown Energy Util | 0.15 | 0.32
Workload distribution
Brown Energy Utilization
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 44.0 | 45.0
 | 0.25 | 0.14 | 0.072 | 0.04 | 0.03 | 0.015 | 0.016
Number of data centers
93% Improvement
Correlation coefficient alone cannot
be a good measure for variability
Variability is determined by the wind farm
with larger wind power generation
In contrast, coefficient of variation is a
much better metric fro variability
Good selection of
wind farms
Bad selection of
wind farms
Achieve nearly “entirely green”