## Slide 1
Bringing the Multicore Revolution to Safety-Critical Cyber-Physical Systems
Motivation
Shared hardware like caches & TLBs introduce timing unpredictability for real-time systems (RTS).
Worst-case execution time (WCET) analysis for RTS with shared hardware resources is often so pessimistic that the extra processing capacity of multicore systems is negated.
Different levels of assurance are required for different criticality tasks.
Problem
Cache Management – Solution & Results
1University of North Carolina Chapel Hill 2North Carolina State University
PIs: Dr. James Anderson1 & Dr. Frank Mueller2
Students: Bryan Ward1, Jonathan Herman1, Namhoon Kim1, Shrinivas Panchamukhi2
CPU
L1 cache
L2 cache
Main memory
a) Memory ref hits in L1 cache – Access latency: 1-4 cycles.
CPU
L1 cache
L2 cache
Main memory
b) Memory ref misses L1 & L2 cache – Access latency: 40-100 cycles.
c) Memory ref misses in TLB – Access latency: +1000 cycles.
Tighter WCET estimates can be established if we know which references hit in the cache and which do not.
Other shared resources like TLBs show similar timing unpredictability.
Solution
Our solutions focus on two shared resources: shared caches and TLBs.
TLB Coloring:
  Control the allocation of memory so that real-time tasks will not interfere with one another in terms of DTLB conflicts.
  Make DTLB misses more predictable.
  Enable static timing analysis tools to compute tight bound on WCET.
Cache Management:
  Leverage the fact that only highly critical components require conservative provisioning.
  Provide “temporal isolation” across criticality levels.
  Apply a multiprocessor real-time synchronization protocol to manage cache lines.
  Enable schedulability gains by reducing WCET.
MC2 (mixed-criticality on multicore) architecture
Mixed-Criticality System
Conclusions
Designed TLB coloring techniques to support contiguous page allocations.  eliminate DTLB misses.
Evaluated on Intel 16 core platform.
Conducted experiments using synthetic benchmark, Malardalen benchmark, and MiBench.
Provided task isolation in terms of DTLB conflicts.
Re-implemented a mixed-criticality scheduler in LITMUSRT to support cache management.
TLB Coloring – Solutions & Results
Design
Assign the same color to pages that map to the same DTLB set.
To support greater than page size allocations, R sets are reserved. (Max contiguous allocation = PAGE_SIZE * R)
Data Structures and Implementation
tlb_malloc_init()
  Sets aside huge virtual address space
tlb_malloc(size, color)
  Allocates memory region of size bytes of a particular color
  Serves allocations from the pool set aside by tlb_malloc_init
tlb_free(color)
  Deallocates memory
  Adds memory back to the pool
malloc - non uniform utilization of DTLB sets
tlb_malloc - predictable
Results
Zero misses if tasks use tlb_malloc
CPU 0
CPU 1
CPU 2
CPU 3
CE
CE
CE
CE
P-EDF
P-EDF
P-EDF
P-EDF
G-EDF
Best Effort
A
B
C
D
Ongoing Work
Assign colors to pages to control the mapping address of memory pages.
Higher-criticality tasks should not be affected by lower-criticality tasks.
Request tokens to reserve cache lines before loading pages.
Implement MC2 scheduler in LITMUSRT.
Enable budget enforcement using container abstraction within the OS.
Trap page fault when a job accesses a page for the first time to request token.
Determine whether cache bypass can be selectively applied.
Devise needed schedulability analysis.
Cache Management
Color 0
Way 0
Way 1
…
Way 7
…
Color M
CPU 0
CPU 1
CPU 2
CPU 3
Partition caches to eliminate interference across processors for Levels A and B.
Global tasks at Level C require tokens to reserve cache lines.