CPS:Small:
Dynamically Managing the Real-time Fabric of a Wireless Sensor-Actuator Network

Project Number: CNS-09-31195

Investigators: M.D. Lemmon and X. Hu

Start Date: 9/1/2009 – 8/31/2012

Wireless sensor-actuator networks (WSAN) consist of numerous sensing and actuation devices that share information over an ad hoc wireless communication network.   WSANs may be used to manage networked systems that distribute goods and services over large spatially distributed domains.  Examples of such systems include the national power grid, ground/air traffic networks, and water/gas distribution networks.

This project studies the implementation of feedback control algorithms over WSANs, particularly with regard to the management of large-scale networked systems such as the electric power grid or water distribution networks.  Controlling such physical processes usually requires some form of hard real-time support, so that each packet of feedback data must be serviced within a specified deadline.  It has, in practice, been difficult to provide such guarantees in real-life wireless networks.  This project addresses that issue by developing algorithms that allow control applications and wireless network nodes to work together in maximizing application performance subject to hard real-time service constraints.

The algorithms being developed by this project are based on a three-prong approach.  First, one must control network interference to provide a stable platform upon which real-time guarantees become possible.   Second, network flows must be scheduled in a manner that achieves the real-time capacity of the stabilized network [1,2,3].  Third, if the network’s quality of service falls below application requirements, then the application must use controllers that demand less of network resources [4,5].   These approaches are being developed through a novel extension of distributed power control algorithms to real-time flows, recent advances in elastic scheduling of real-time tasks, and recent advances in our understanding of sporadic sampled-data control systems.   This project’s algorithms will be implemented on a wireless test bed consisting of software-defined radios and/or sensor network modules (Mica).

The impact of this project is being broadened through interactions with local industry and graduate curriculum development.  A first year graduate course (EE67036) on cyber-physical systems focusing on modeling, verification, and control synthesis has been developed and a textbook is being written from the course’s lecture notes.   The project is also working with two small businesses to develop real-time WSAN applications for environmental monitoring (EmNet LLC) and microgrid control (Odyssian LLC).

References

- Shengyan Hong, Xiaobo Sharon Hu, and M.D. Lemmon, An adaptive approach to reduce control delay variations, Real-time Systems Symposium, work-in-progress session, Washington D.C., December 2009.

- S. Hong, X.S. Hu, and M.D. Lemmon, Reducing Delay Jitter of Real-time Control Tasks through Adaptive Deadline Adjustments, Euromicro Conference on Real-time Systems (ECRTS10), Brussels, Belgium, July 2010

- J. Yi, C. Poellabauer, X.S. Hu, and L. Zhang (2010), Minimum Bandwidth Reservations for Periodic Streams in Wireless Real-time Systems, accepted for publication in IEEE Transactions on Mobile Computing, 2010.

- Q. Ling and M.D. Lemmon, A necessary and sufficient feedback dropout condition to stabilize quantized linear control systems with bounded noise, to appear in IEEE Transactions on Automatic Control, November 2010

- Q. Ling and M.D. Lemmon, Input-to-state stabilizability of quantized linear control systems under feedback dropouts, Proceedings of the American Control Conference, Baltimore, 2010