## Slide 1
Converting Multi-Axis Machine Tools into Subtractive 3D Printers
by using Intelligent Discrete Geometry Data Structures
designed for Parallel and Distributed Computing
Model Representation
Machining Simulator
Multi-axis Machining
Root
Cell
Subcell
Cell
Cell
Cell
Subcell
Subcell
Subcell
Subcell
Tree-like to cluster resolution at the boundary where it is needed.
Voxel-like at leaves to provide constant time inside/outside testing.
Tailored specifically for parallel processing such as GPUs
Intelligent Discrete Geometry Data Structures
Physical
Application
Logical
Input from Target &
Strategy
Conceptual
Software Platform
Data & load Structure
Parallel Processing
GPU Processing
CAD
Optimize
Feature & Function
Product
Quality
Performance (Time & Cost)
Automation
Business Target
Machine Structure
Multi-Axis Component
Parts & Tools
Vision &
Metrics
Interactive 3D Rendering of Model
A tool positioned on the offset volume must assume an orientation that avoids collisions.
An “accessibility map” provides allowable orientations for the tool.
Stacked in sequence, the accessibility maps form an accessibility space.
Tool Orientation and Tool Retractions
Offset volume provides surface where a tool of a given radius travels without over/under-cutting.
Successive offset volumes provide a sequence of XYZ points for a tool path.
Tool Positioning
System Integration Scope
System Components
Software Interface
Resulting Parts
Iterative Toolpath Generation
Axes Configuration
&
Kinematics
Multi-axis Machining Simulation
Input Mesh (STL)
Voxelized Model
Multi-axis CNC Machine
Machined Part
G-codes
Sometimes the path encounters a “dead end” in accessibility space and must jump to a new open “tunnel” in order to continue.
These events in accessibility space correspond to tool retractions.
Demonstration of iterations of volume removal:
G-code simulation with performance graphs: