## Slide 1
Bipedal Robot
Robot model
A 12 diminsional model for AMBER 2 where is the joint angle [rad], is the joint velocity [rad/s].
Specifications
Joint torques required to meet
desired bounds.
Swing foot shouldn’t scuff
before the end of a step.
The feet are required to remain
flat during a walking gait.
Correct-by-design controller
Simulation results for 1.5 seconds.
Next Steps
Move from fully actuated to under actuated bipedal robots.
Compositional correct-by-construction synthesis.
Lane Keeping
Lateral-Yaw model
where y is lateral displacement [m], and are longitudinal and lateral speed [m/s], and are yaw and desired yaw angles [rad], and are yaw and desired yaw rates [rad/s], is steering angle [rad].
Specifications
Provide steering input to keep
the car centered in the lane.
Displacement from center
shouldn’t exceed 0.9 meters.
Correct-by-design controller
Moving with constant longitudinal velocity [100 km/hr].
Lane keeping such that lateral displacement is less than 0.9 meters.
Objectives
Develop a formal framework for correct-by-construction software synthesis for highly dynamic CPSs.
Realize this framework experimentally for an advanced vehicle safety system and a bipedal robot.
  Highly dynamic CPS: Cyber-physical systems where the difference between stable (safe) behavior and catastrophic (unsafe) behavior occurs in milliseconds
  Correct by construction: “Specify and compile” instead of “design and verify”.
  Examples: Adaptive cruise control (ACC); Lane keeping; Landing a UAV on an aircraft carrier; Bipedal robot rushing through rubble.
  State of the art:
  Control software development for highly dynamic CPSs relies on trial and error;
  small changes in hardware often require extensive labor-intensive retesting and redesign of software;
  no guarantees on closed-loop behavior.
Key Challenges
Curse of dimensionality (e.g., nonlinear models greater than dimension 2)  Hybrid models comprised of motion primitives and low-level control software.
Environmental uncertainty (e.g. terrain variation)  adding adversarial non-determinism to the discrete abstractions; 2-player game for robust synthesis.
Team
Advisors from Ford and Toyota.
Prof. Necmiye Ozay and Postdoc Xiangru Xu (UMich), Postdoc Eric Dallal (UCLA).
Students: Yuxiao Chen and Petter Nilsson (UMich), Omar Hussien (UCLA), Forrest Berg (TAMU) and Albert Wu (CMU).
Frontier: Correct-by-Design Control Software Synthesis for Highly Dynamic Systems
Jessy Grizzle and Huei Peng
University of Michigan
Paulo Tabuada
UCLA
Aaron Ames
Texas A&M
Hartmut Geyer
Carnegie Mellon
Source: Forbes
Time (s)