## Slide 1
Cyber-Physical Cloud Computing
cpcc.berkeley.edu
PI: Raja Sengupta(a)
Co-PI: Christoph Kirsch(b), Karl Hedrick(c)
(a)Systems Engineering, Department of Civil and Environmental Engineering, University of California, Berkeley. Email: rajasengupta@berkeley.edu
(b)Department of Computer Sciences, University of Salzburg. Email: ck@cs.uni-salzburg.at
(c)Department of Mechanical Engineering, University of California, Berkeley. Email: khedrick@me.berkeley.edu
  Virtual Vehicle (VV): Virtual Machine + Virtual Speed.
  Physical-mobility, Cyber-mobility
  Theorem 1: Each VV is a GI/GI/1 queue.
  Voronoi Allocation:
  Theorem 2: Each RV is a ΣGI/GI/1 queue.
Scheduling: Earliest Virtual Deadline First (EVDF)
  Theorem 3: EVDF achieves minimum tardiness.
  Tardiness = max{Actual completion time – Virtual deadline, 0}
Gain: # VVs / # RVs at a given Performance Isolation
  Multiplexing gain, Migration gain
  Conclusion:
  High migration gain and high performance isolation.
  Economy of scale: migration gain increases with # RVs.
  Migration gain happens when traveling, not standing still.
  Migration cost is bounded.
BigActor Model is a bridge between programs and machines with dynamic structure (location and connectivity)
BigActors are Actors [1] hosted at a Bigraph abstraction of the world [2] that can:
  Compute, communicate, observe, control and migrate
  BigActors – Ubiquitous Computation over Worlds with Dynamic Structure
Runtime environment for mobile robotics:
  BigActors Scala DSL - API
  bigraphDriver: abstracts the world as a bigraph
  brrDriver: handles the execution of control actions
  gateway: distributed bigraph estimation and communication
Case study: networked robotics
Example 1: logical space programming
Example 2: handover
"gotoOil" hosted_at "uav0" with_behavior{
loop{
MOVE_HOST_TO oilSpill
}
}
autopilotWaypointCtr(Lat0,Long0,Alt0,radius)
autopilotWaypointCtr(Lat1,Long1,Alt1,radius)
autopilotWaypointCtr(Lat2,Long2,Alt2,radius)
autopilotWaypointCtr(Lat3,Long3,Alt3,radius)
…
"handover" hosted_at "GCS0" with_behavior{
HANDOVER uav0 TO GCS1
}
=>
[1] R. Milner, “The Space and Motion of Communicating Agents”, Cambridge, 2009.
[2] G. Agha, “Actors: a model of concurrent computation in distributed systems”, MIT Press, 1986.
[3] E. Pereira et al., “Bigactors - A Model for Structure-aware Computation,” in ACM/IEEE 4th International Conference on Cyber-Physical Systems, 2013.
[4] E. Pereira et al., “Modeling and controlling the structure of heterogeneous mobile robotic systems: A bigactor approach,” in 2013 IEEE International Systems Conference (SysCon), 2013.
[5] E. Pereira et al., “A Networked Robotic System and its Use in an Oil Spill Monitoring Exercise,” in Swarm at the Edge of the Cloud Workshop (ESWeek’13), 2013.
=>
  Supported in part by:
Demo: oil spill monitoring
Satellite image. Courtesy of EMSA
UAV Onboard image
UAV Alfa Extended
Mobile Control Station