## Slide 1: Don Winter VP - Flight & Systems Technology Boeing Research & Technology
Cyber-Physical System (CPS) Challenges in the NextGen

## Slide 2: Boeing is a Key CPS Stakeholder
The Boeing Company is working a rich set of application areas that are benefiting from CPS research
  Air (military and commercial)
  Space (high-reliability applications)
  Land (networking land elements)
  Air Traffic Management
Applications involve multiple, networked CPS systems
  Safety-critical aspects
  Security
  Need for predictability in face of dynamic environments
Aircraft platforms
  Commercial
    Stringent certification and V&V processes and standards
  Military
    Piloted and autonomous vehicles
    Support all services
    Unmanned vehicles in NAS
    Varying levels of V&V requirements

## Slide 3: Aviation CPS Applications: Future Aircraft and NextGen
NextGen
Future Aircraft
Abstract System Architecture
Tight integration within aircraft, and between aircraft and off-board systems

## Slide 4: NextGen is a Large-Scale CPS
Landing
Enroute
Today’s NAS
(Loose Integration, “Stovepiped”)
Cyber
Cyber-Physical Interactions
NextGen
(Tight Integration)
Physical
Cyber
Transformation
Taxi
Takeoff
NextGen uses “cyber,” i.e., networking, software, computing, to tightly weave taxing, takeoffs, enroute flight paths, and landings

## Slide 5: Tight Integration in the NextGen: Examples
Higher Precision Flight Anywhere
Higher Precision Common Awareness
Improved Capacity,
Safety & Efficiency
Improved Agility,
Security & Economy
Performance-based Operations
Dynamic Seamless Airspace
Enabled Applications/Services
Enables
Enhanced CNS
(e.g., GPS, ADS-B)
System Wide Information Management
Information Infrastructure
3X+ capacity
Environmental benefits
$10-30B/yr global savings
Global interoperability
Accident reduction
Threat deterrence
Create
Transformed Global Air Traffic System

## Slide 6: Cyber-Physical Interactions in the NextGen: Examples
FOC
Aircraft
In-flight coordination
ANSP
Flight Operations Centers
Service Providers
Airspace
Coordination for airborne
sensing and action webs
Control and coordination for
separation assurance and
hazard avoidance
Control and coordination
for flight safety and efficiency
Cyber components? Aircraft digital communications; weather/traffic forecast, flight planning/optimization algorithms; situation awareness and decision support software
Physical components? Mobile aircraft; dynamic airspace traffic, weather, pollution, noise; pilots, air traffic controllers, airlines crew

## Slide 7: Grand CPS Challenges of the NextGen
Aircraft and Airspace
Computing
Highly collaborative
Advanced CPS applications monitor and effect change in aircraft and airspace, automatically and/or with the human-in-the-loop
Presence of cyber and physical risks/threats to performance
How to study the joint dynamics of this collaborative system?
How to provide deterministic, highly predictable and provable behavior for this collaborative system?
Software
Networks
Command and
Control
Formation
Sensor
Processing
Enabled Services/Applications
Crew
(pilots, traffic controllers, etc.)
Seamless, rich interaction
Cyber
Risks and
Threats
(e.g., system
failures,
disruptions)
Physical
Risks and
Threats
(e.g., weather,
solar flares)

## Slide 8: CPS Research Challenges in the NextGen (1)
Extremely heterogeneous with many types of aircraft and users – Need to consider aircraft limits & user preferences in CPS solutions
Mixed criticality for information assets – Need prioritization of cyber and physical resources; functions to handle information of various trust levels; cyber security advances
Networking employed from in-aircraft system to global system scales – Need worldwide interoperability for aviation networks; advances in communications, signal processing and wireless security, data fusion
Large systems-of-systems for sharing critical real-time data – Need advances in cross-domain interoperability, assured timely end-to-end information exchange, distributed coordination
Verification, validation and certification are essential – Need efficient V&V techniques; advances in visualization and virtual reality, security versus safety, and software development assurance

## Slide 9: CPS Research Challenges & Implications for NextGen (2)
Complexity at multiple temporal/spatial scales – Need advances in data mining, sensor network, operations research, weather models
High degrees of automation, control loops close at all implemented scales – Need advances in human-automation interface, crew fatigue management, close coupling of networking with aircraft mobility control, air traffic control algorithms, cyber-physical security
Autonomous operations and national security are vital – Need advances in sense-and-avoid and control of unmanned systems; integrated airspace surveillance capability
Legacy system integration and migration – Need new solutions to be reverse and forward compatible
Longevity is a must, since system lifetimes is several years to decades – Solutions must have a long lifespan or be inexpensively and independently upgradeable

## Slide 10: Operations Enabled With ADS-B
Standard Longitudinal
Separation Requirement
ITP Aircraft
Blocking Aircraft
ITP Criteria
FL360
FL360
FL360
In-Trail Procedures
Merging and Spacing,
Surface Operations,
and Closely-Spaced
Parallel Approaches
Reduced-Separation in
Non-Radar Airspace
Notes: Because of lack of effective surveillance, aircraft in oceanic regions operate under procedural control with large separation criteria. In this particular scenario, where we have multiple aircraft at different altitudes, the blue aircraft would not be permitted to climb to a more fuel-efficient altitude, say FLT 360, because its proximity to the red aircraft is less than the standard longitudinal separation.
The In Trail Procedures concept calls for the blue airplane to be equipped with an appropriate spacing application based on ADS technology (potentially ADS-C or ADS-B). This self-spacing capability is expected to reduce the required longitudinal separation between aircraft, and allow the blue aircraft to climb through FL 350 occupied by the red aircraft, in spite of less than standard longitudinal separation.
This procedure can also be used for descending through an occupied altitude, although the opportunities for benefits are much less common than for a climb situation. In-trail climb and descent procedures present a significant opportunity for improving flight time, fuel burn and emissions by enabling airplanes to obtain desired altitudes in congested oceanic airspace.
This can have significant benefits for very long haul flights such as between Asia and Europe, North America and the South Pacific and across the polar region between Asia and North America. In some cases such fuel-saving procedures can prevent a diversion, which is costly for the airlines and an undesirable experience for airline passengers.

## Slide 11: Continuous Descent Approaches
Notes: Current operational procedures call for airplanes to be gradually stepped down from its TOD point to touchdown, as shown by the red ribbon. Repeated idling and spooling up of engines during the descent phase is not fuel efficient and offers the opportunity for fuel savings.
The optimal descent into an airport means flying at cruise altitude until the exact point at which bringing the engines to idle will result in the least fuel burn until the engines are spooled up just before touchdown. As shown by the green ribbon – and these procedures have been labeled Continuous Descent Approaches.
Sometimes, ill-conceived noise abatement procedures also result in leveling airplanes during descent which in turn means engines are spooled-up, flaps and perhaps gear are deployed all of which results in more noise. Better designed lateral flight profiles, combined with Continuous Descent Approaches can result in lower fuel burn, fewer emissions and less noise. This takes us to the next concept called Tailored Arrivals.
Note:
Because perfect information about winds does not exist and because terrain can sometimes get in the way, attaining the optimum descent may remain an ideal. We can, however, come much closer to the ideal by eliminating many of the inefficiencies that have been engineered into the system over time. In many places airspace design results in step-downs which cost fuel and cause greater emissions than are necessary. that is an arrival much closer to the ideal. The vertical profile improvements are combined with horizontal arrival improvements in a concept called ….. (Tailored Arrivals).

## Slide 12: A Near-Term Example – Tailored Arrivals
Tailored arrivals are CDAs, or near-CDAs, flown on 4D paths that are shaped for local constraints and timed for merging traffic.
Top of Descent
DANKS
CHAPI
ARBEY
BUNKY
28,000 ft
300 kt
11,000 ft
300 kt
9,000 ft
190 kt
SFO
SYD
MEL
AMS
Typical arrival

## Slide 14: Tailored Arrival Trial at SFO