## Slide 1
* North Carolina State University, +University of Illinois Urbana Champaign, and ++RENCI, University of North Carolina
Aranya Chakrabortty*, Frank Mueller*, Rakesh Bobba+, Nitin Vaidya+ and Yufeng Xin++
Distributed Asynchronous Algorithms & Software Systems For Wide-Area Monitoring of Power Systems
Project Goal
Technical Approach
Distributed Oscillation Monitoring
Distributed Middleware
Fault-Tolerance & Cyber-Security
Experimental Testbed
PMU
PMU
PMU
PMU
PMU
PMU
To translate current state-of-art centralized processing algorithms for wide-area monitoring of large power grids using large volumes of Synchrophasor data to a completely distributed cyber-physical architecture.
Intellectual Merits:
Distributed oscillation monitoring
Distributed voltage
monitoring
3. Distributed middleware
4. Fault-tolerance
Experimental verification using
Exo-GENI network
6. Real-time testing of QoS
and cyber-security
Proposed Distributed Cyber-Physical Architecture for PMU-PDC Communication:
Dynamic Rate Control Problem (DRCP):
- Find optimal PMU data exporting rates, and frequency of information exchange between local PDCs and inter-regional PDCs to minimize computation error between centralized and distributed estimation
Dynamic Link Assignment Problem (DLAP):
- Find optimal communication topologies in real-time connecting local and inter-regional PDCs to maximize computational speed for the overall global estimation/monitoring/control problem.
Problem statement: Compute power flow oscillation frequencies (eigenvalues), mode shapes (eigenvectors), damping, and residue from PMU measurements using distributed algorithms implemented via DRCP and DLAP.
Power System Dynamic Model
Two types of consensus algorithms in the presence of faults. These algorithms are useful for coordinating agents in a distributed manner:
- Iterative approximate consensus under Byzantine link faults
- Iterative convex hull consensus under crash and
Byzantine node faults
Evaluation of the impact of Byzantine failures on ADMM, and exploration of potential mitigation mechanisms
Broader Impacts
Participated in Smart America Challenge 2014 Initiative of NIST and US White House
Federated BEN-WAMS: Multi-vendor PMU-based hardware-in-loop simulation testbed at NCSU and DETERLab at Uniiv. of Southern California to showcase resiliency of ADMM based wide-area oscillation monitoring
Smart America Challenge 2014 and US Ignite 2014 demos
Undergraduate, K-12 and minority education via Science House and FREEDM ERC programs at NC State
Undergraduate summer internship at Information Trust Institute at UIUC
Industry collaborations with power utilities and vendors such as SCE
1: Update both primal and dual estimation variables at every local control center:
2: Gather the values of at the central ISO
3: Take the average of at the central ISO
4: Broadcast the average to local control centers and iterate to Step 1
New Algorithms and Results using ADMM
PDC 1
PDC 3
PDC 4
PMU
PMU
PMU
PMU
Central PDC at ISO
θ11(t)
θ12(t)
θ31(t)
θ32(t)
θ21(t)
θ22(t)
θ41(t)
θ42(t)
Area 1
Area 3
Area 2
Area 4
PDC 2
Area 1
Area 3
PMU
PMU
PMU
PMU
θ11(t)
θ12(t)
θ31(t)
θ32(t)
θ21(t)
θ22(t)
θ41(t)
θ42(t)
Area 2
Area 4
Communication
Graph G
PDC 3
PDC 2
PDC 4
PDC 1
Area 1
PDC 1b
PMU
θ11b(t)
θ21b(t)
PDC 1a
PMU
θ11a(t)
θ21a(t)
PDC 1c
θ11c(t)
θ21c(t)
PDC 3b
PMU
θ13b (t)
θ23b (t)
PDC 3a
PMU
θ13a (t)
θ23a (t)
PDC 3c
θ13c(t)
θ23c (t)
PDC 2a
PMU
θ22a(t)
θ12a(t)
PDC 2b
PMU
θ22b(t)
θ12b(t)
PDC 2c
PDC 4a
PMU
θ24a (t)
θ14a(t)
PDC 4b
PMU
θ14b (t)
θ24b (t)
PDC 4c
θ24c(t)
θ14c(t)
θ22c(t)
θ12c(t)
Central PDC at ISO
Area 3
Area 2
Area 4
Distributed LS problem
Hacked
PDC 1
PDC 3
PDC 4
PMU
PMU
PMU
PMU
Central PDC at ISO
θ11(t)
θ12(t)
θ31(t)
θ32(t)
θ21(t)
θ22(t)
θ41(t)
θ42(t)
Area 1
Area 3
Area 2
Area 4
PDC 2
Problem statement: Develop distributed middleware to support DRCP and DLAP algorithms for oscillation monitoring and transient stability.
Store recent PMU data
Supply PMU data with predictable delays
Idea: Real-time distributed storage (RT-DHT) utilizes
- Fault-tolerant network overlays - Chord-like ring + finger pointers - Multiple replicas of data  faults OK
- Prioritized requests urgent algorithm served first
- Deterministic wide-area networks
Infrastructure
- Cloud computing
- Software Defined Networks (SDN)
Experiments: BEN, Exo-GENI, and GENI