## Slide 1: Internet of Things Enables a Cyber-Physical Systems Approach to Lighting
2
December 2014 Philips Research Confidential
Abhishek Murthy*, Yong Yang, Dan Jiang, Talmai Oliveira, and Dave Cavalcanti
Philips Research North America
*abhishek.murthy@philips.com
NSF Workshop on Big Data Analytics in CPS: Enabling the Move from IoT to Real-Time Control
April 13, 2015
Notes: Please insert a characteristic picture for your topic and crop it to 140 mm x 240 mm to fit template
Check if topic title is appropriate
Insert a subtitle that inspires / triggers / hints the reader in the direction that you are aiming for, this can be visionary / high leve / long term oriented

## Slide 2: Outline
Internet of Things (IoT): an Enabler for Smart Cities
Lighting has come a long way
Lighting-Enabled IoT Applications
Networking Issues
Applications: Light-on-Demand
Applications: Traffic-Adaptive Lighting
Conclusions

## Slide 3: IoT: an Enabler for Smart Cities
Cities are already using IoT to solve various problems
Traffic congestion (NYC)
Crime prediction (Chicago)
Smart grids (Chattanooga)
Civic repairs (Boston)
Cities expected to spend around 12 Billion dollars over the next ten years
Incremental projects, not overly ambitious, tend to yield results faster
Source: Cities Get Smarter, MIT Technology Review, February 2015

## Slide 4: Lighting: a widespread and dense urban infrastructure
52.5 million roadway fixtures in the US [1]
  26.5 million streetlights
  26.1 million highway fixtures
  262,000 streetlights in NYC [2]
Indoor + Outdoor: 19% of total energy budget, 2014 [3]
  52.8 TWh for roadway lighting, 51.1 TWh for parking and garage lights
Combined energy usage equivalent of 167 million barrels of oil, 71.6 million metric tonnes of [1]
Conventional streetlights in NYC

## Slide 5: Lighting has come a long way …
Power-efficient Solid-State Technology
Remote monitoring & control
Connected
Aware (sensor-enabled)
Existing Lighting-Related Technologies
Adaptive
Dimming Schedules

## Slide 6: Lighting-Enabled IoT Applications
IP Network
Intelligent Transportation Systems
Wireless Mesh-Based lighting network
Gateway
Wireless Sensor Nodes
Adaptive Energy-Efficient Light-on-Demand
Heterogeneous Spatio-Temporal Data
Value-Added Services
Analytics
Traffic Monitoring
Road Surface Monitoring
Pollution Monitoring
Cloud-Based Data Acquisition, Processing & Actuation

## Slide 7
Network capacity and quality-of-service crucial for value-added services beyond lighting
Networking Issues
Heterogeneous Wireless Lighting Networks
IP Network
Central Mgmt. Systems
Gateway
Mesh Networks
Unlicensed spectrum, cheaper
Locally managed
Cellular Networks
Highly reliable
Guaranteed quality of service

## Slide 8
Capacity Analysis Simulations
Grid-based topology of light poles equipped with 802.15.4g radios
Multiple sources send data to sink, a gateway at the center of hexagonal regions
Networking Issues
 |  | IEEE 802.15.4 |  | IEEE 802.15.4g |  |  | 
Data rates (Kbps) |  | 40 | 250 | 50 | 200 | 400 | 800
SNR |  | 0dB | 9dB | 6dB | 9dB | 15dB | 21dB
# light Poles | 1K | 38 | 15 | 32 | 8 | 4 | 2
 | 5K | 200 | 87 | 190 | 58 | 34 | 17
 | 10K | 403 | 177 | 389 | 122 | 89 | 46
Throughput (KB) per light pole per day: denser topologies give higher throughputs.
Delay (Minutes) in delivering 5KB of load per light pole: only delay-tolerant applications can be supported.
Gateways with hexagonal coverage (sinks)
Grid-based topology for lighting networks
Chart: Throuput per lightpole per day
| 40.0 | 250.0 | 50.0 | 200.0 | 400.0 | 800.0
1K | 187.65 | 483.83 | 224.92 | 899.67 | 1778.7 | 3477.7
5K | 35.89 | 82.43 | 37.86 | 124.03 | 210.34 | 411.25
10K | 17.85 | 40.45 | 18.51 | 58.64 | 80.79 | 155.99

## Slide 9
Dim the LED-based lights by default, at say a parking lot
Camera-based sensors detect motion, trigger light controllers to maximize light levels
Triggers flooded over a mesh network to all the lights
Up to 87% energy savings over traditional lighting
Applications: Light-on-Demand
Successful Dept. of Defense project at Fort Sill, OK (project # EW201141)

## Slide 10
Roadway lighting affects driving conditions
Federal Highway Administration: potential to decrease lighting levels by up to 50% safely [4]
Traffic profile: either updated in real time or use historical trends
The two approaches are not significantly different for most of the roadways
10% - 40% energy savings possible
Applications: Traffic-Adaptive Lighting

## Slide 11
Connected outdoor lighting can help save energy and reduce emissions
CPS approaches to lighting: Light-on-Demand, Traffic-Adaptive Lighting
The resulting mesh network can be used for data-enabled applications beyond lighting: environmental sensing, crowd monitoring, etc.
Networking issues: capacity analysis of mesh-based link layer technologies
Other issues
  Interoperability
  Systems approaches for scalability
Conclusions

## Slide 12: References
NEEA Study: Technology and Market Assessment of Networked Outdoor Lighting Controls, Northwest Energy Efficiency Alliance, 2011.
Green Light, Sustainable Street Lighting for NYC, New York City Department of Transportation.
2010 U.S. Lighting Market Characterization, U.S. Department of Energy, 2012.
Design Criteria for Adaptive Roadway Lighting, U.S. Department of Transportation, Federal Highway Administration, 2014.