## Slide 1: Models of Time for a Computational World
Edward A. Lee
Robert S. Pepper Distinguished Professor UC Berkeley
National Workshop on The New Clockwork for Time-Critical Systems
October 25, 26, and 27, 2012
Baltimore, Maryland
Key collaborators:
Patricia Derler
John Eidson
Slobodan Matic
Sanjit Seshia
Yang Zhao
Michael Zimmer
Haiyang Zheng
Jia Zou
Sponsors:
Bosch
MARCO/DARPA
NSF
NSA
National Instruments
OSD/NRL
Thales

## Slide 2: Bridging Discrete and Continuous
Computation is discrete
Time is a continuum
Naïve bridges between the two fall short

## Slide 3
What is the momentum of the middle ball as a function of time?
Notes: \textbf{p}(t) = m \textbf{v}(t)

## Slide 4
What is the momentum of the middle ball as a function of time?
It might seem:
Notes: \textbf{p}(t) = m \textbf{v}(t)
\textbf{v}(t) = 0 \quad \Rightarrow \quad \textbf{p}(t) = 0

## Slide 5
But no, it is:
where ti is the time of collision
Notes: \textbf{v}(t) = \left \{ \begin{array}{ll}
\textbf{K}, & t = t_i \\
0 & \mbox{otherwise}
\end{array} \right .

## Slide 6
Since position is the integral of velocity, and the integral of v is zero, the ball does not move.
K
ti
Notes: \textbf{v}(t) = \left \{ \begin{array}{ll}
\textbf{K}, & t = t_i \\
0 & \mbox{otherwise}
\end{array} \right .

## Slide 7
A discrete representation of this signal with samples is inadequate.
K
ti
Notes: \textbf{v}(t) = \left \{ \begin{array}{ll}
\textbf{K}, & t = t_i \\
0 & \mbox{otherwise}
\end{array} \right .

## Slide 8: Samples yield discrete signals
A signal is sampled at tags
t
t0
t1
t2
t3
ts
...
A signal s is discrete if there is an order embedding from its tag set  ( s ) (the tags for which it is defined and not absent) to the natural numbers (under their usual order).

## Slide 9
No discrete subset of real-valued times is adequate to unambiguously represent this signal.
K
ti
Notes: \textbf{v}(t) = \left \{ \begin{array}{ll}
\textbf{K}, & t = t_i \\
0 & \mbox{otherwise}
\end{array} \right .

## Slide 10
There is no semantic distinction between a discrete event and a rapidly varying continuous signal.
K
ti
Notes: \textbf{v}(t) = \left \{ \begin{array}{ll}
\textbf{K}, & t = t_i \\
0 & \mbox{otherwise}
\end{array} \right .

## Slide 11: Simulink/Stateflow cannot accurately model such events.
Transient States
The simulator engine of Simulink introduces a non-zero delay to consecutive transitions.
In Simulink, a signal can only have one value at a given time. Hence Simulink introduces solver-dependent behavior.

## Slide 12: Ptolemy II uses Superdense Time [Maler, Manna, Pnuelli, 92] for Continuous-Time Signals
At each tag, the signal has exactly one value. At each time point, the signal has a sequence of values. Signals are piecewise continuous, in a well-defined technical sense, a property that makes ODE solvers work well.
Initial value:
Intermediate value:
Final value:
http://ptolemy.org
Notes: \textbf{v}\colon (\rr \times \nn) \to \rr^3
\textbf{v}(t_i, 0) = 0

## Slide 13: Consequences of using Superdense Time
Transient states are well represented:
Infinitessimals (even Dirac delta functions):

## Slide 14: More Consequences: Hybrid System
Finite State Machine
Dyanmics 1
Dynamics 2

## Slide 15: Transitions between modes are instantaneous
In the signals at the right, the velocities and accelerations proceed through a sequence of values at the times of the collisions and separations.

## Slide 16: Superdense Time
The red arrows indicate value changes between tags, which correspond to discontinuities. Signals are continuous from the left and continuous from the right at points of discontinuity.

## Slide 17: Modal Models and Multiform Time
Once we have a clean, instantaneous handoff between modes, a question arises about how to model time is a dormant mode.
Actor
Refinement
FSM
State
Transition
Refinement
Ports
Ports
When this mode is inactive, should time advance?

## Slide 18: The Modal Model Muddle
It’s about time
After trying several variants on the semantics of modal time, we settled on this:
A mode refinement has a local notion of time. When the mode refinement is inactive, local time does not advance. Local time has a monotonically increasing gap relative to environment time.

## Slide 19: MultiForm Time in Ptolemy II
suspend
resume
reference time
local time
In Ptolemy II Modal Models, Time is suspended and resumed
Local time inside a mode refinement
Environment time
Notes: Edward A. Lee, “Finite State Machines and Modal Models in Ptolemy II,”
EECS Department, University of California, Berkeley,
Technical Report No. UCB/EECS-2009-151, November 1, 2009

## Slide 20: Variants for the Semantics of Modal Time that we Tried or Considered, but that Failed
Mode refinement executes while “inactive” but inputs are not provided and outputs are not observed.
Time advances while mode is inactive, and mode refinement is responsible for “catching up.”
Mode refinement is “notified” when it has requested time increments that are not met because it is inactive.
When a mode refinement is re-activated, it resumes from its first missed event.
All of these led to some very strange models…
Final solution: Local time does not advance while a mode is inactive. Monotonically growing gap between local time and environment time.

## Slide 21: Once we have multiform time, we can build accurate models of cyber-physical systems
Notes: We want to run for two seconds.
The fact that it runs for two seconds is a combination of the program and hardware.

## Slide 22: Engineers model physical dynamics using differential-algebraic equations.
The variable t represents an idealized Newtonian notion of time.

## Slide 23: But computational platforms have no access to t. Instead, local measurements of time are used.
A superdense Newtonian notion of time becomes environment time

## Slide 24: Local time within a hierarchy can advance at different rates.
Model uses “oracle time,” which becomes “environment time”
for the subsystems.
Model internally uses local time
Discrete Event MoC
Model internally uses local time

## Slide 25: Clocks drift
Fabrication tolerance
Aging
Temperature
Humidity
Vibrations
Quality of the quartz.
Clock drifts measured in “parts per million” or ppm 1 ppm corresponds to a deviation of 1μs every second
Notes: differences in clocks - epoch defines start of time/reference time, leap second adjustment in UTC, even atomic clocks drift! Keeping precise and accurate time is very difficult.

## Slide 26: MultiForm Time in Ptolemy
reference time
local time
Heaven for engineers.
Local time and environment time are in sync!

## Slide 27: Multiform Time in the Real World
offset
reference time
local time
Reality:
There is an offset between local time and environment time

## Slide 28: Multiform Time in Ptolemy
fast clock
slow clock
reference time
local time
More real: clocks drift

## Slide 29: Multiform Time in Ptolemy
environment time:
te
start time:
se, sl
offset:
o = se - sl
clock rate:
cl
local time:
tl = (te - o) × cl
te
tl
se
sl
o
cl = 1.0
cl’ = 0.5
set clock drift
Even more real: clock drift changes!
Notes: timeresolution: used for precision: every time value is rounded to that precision
All time values are rounded to the nearest multiple of this value

## Slide 30: Multiform Time in Ptolemy
environment time:
te
start time:
se, sl
offset:
o = se - sl
clock rate:
cl
local time:
tl = (te - o) × cl
te
tl
se
sl
o
cl = 1.0
cl’ = 0.5
set clock drift
Ptolemy II provides a hierarchy of local clocks
This can be used, for example, to accurately model time synchronization protocols.
Notes: timeresolution: used for precision: every time value is rounded to that precision
All time values are rounded to the nearest multiple of this value
During this period, the director base class was extended with a local
clock, which keeps track of the local time, i.e. the model time at the
level of the model hierarchy. Local time is related to environment
time, the time of the enclosing model, if there is one. Local time can
be offset from the environment time and evolve at a different clock
rate. Local time and environment time evolve simultaneously. The
director exposes the local clock and parameters to change the clock
value as well as the clock rate in Vergil. These parameters are used
to model clock drift and clock synchronization. Two demos of realistic
applications that typically have drifting clocks and need clock
synchronization were implemented in Ptolemy to illustrate the
concepts: (a) the detection of a fault on a power line between two
substations due to disturbance such as lightening and (b) a
triangulation application that computes the source of a sound.
Ptolemy contains timed and un-timed directors. In un-timed directors,
the time of the local clock never advances.

## Slide 31: Multiform Time is Intrinsic!
Time
Physical
Measured
Relativistic
Newtonian
Microprocessor Clock
Synchronized Clock
NTP
PTP, IEEE 1588
GPS
Master Clock
TAI
Time in physical laws, mathematical, continuous
Time in digital systems
  Circuits, discrete clocks, generating well defined periodic signals
  Clock synchronization
Source: Patricia Derler and John Eidson
Notes: International Atomic Time is a high-precision atomiccoordinate time standard based on the notional passage of proper time on Earth's geoid. It is the basis for Coordinated Universal Time (UTC), which is used for civil timekeeping - weighted average of the time kept by over 200 atomic clocks in over 50 national laboratories worldwide
Coordinated Universal Time (UTC) is the primary time standard by which the world regulates clocks and time
UTC is occasionally adjusted by adding a leap second in order to keep it within one second of UT1, which is defined by the Earth's rotation
NTP: within tens of milliseconds over the public Internet,[1] and can achieve 1 millisecond accuracy in local area networksunder ideal conditions, uses UDP
PTP: sub-microsecond range, cheaper than GPS, also known as IEEE 1588
clock synch: define clock hierarchies, master-slave, where hierarchy talks about the distance from the reference clock/quality, configuration, devices such as atomic (caesium, rubidium) clocks, GPS clocks or other radio clocks, compute transmission time/roundtrip delay

## Slide 32: A Perspective on Time Synchronization
Time synchronization is going to change the world
(again)
1500s
days
Gregorian Calendar (BBC history)
Lackawanna Railroad Station, 1907, Hoboken. Photograph by Alicia Dudek
1800s
seconds
2000s
nanoseconds
2005: first IEEE 1588 plugfest

## Slide 33: Today’s networks
“On August 12, 1853, two trains on the Providence & Worcester Railroad were headed toward each other on a single track. The conductor of one train thought there was time to reach the switch to a track to Boston before the approaching train was scheduled to pass through. But the conductor's watch was slow. As his speeding train rounded a blind curve, it collided head-on with the other train—fourteen people were killed. The public was outraged. All over New England, railroads ordered more reliable watches for their conductors and issued stricter rules for running on time.”
Source: National Museum of American History

## Slide 34: A Cyber-Physical System Printing Press
Hundreds of microcontrollers and an Ethernet network are orchestrated with precisions on the order of microseconds.
Software for such systems can be developed in a completely new way.
Bosch-Rexroth
Time synchronization enables tightly coordinated actions and reliable networking with bounded latency.

## Slide 35: Ptides: Programming Temporally Integrated Distributed Embedded Systems First step: Time-stamped messages.
Messages carry time stamps that define their interleaving
Actors specify computation
http://chess.eecs.berkeley.edu/ptides

## Slide 36: Ptides: Second step: Network time Synchronization
GPS, NTP, IEEE 1588, time-triggered busses, … they all work. We just need to bound the clock synchronization error.
Assume bounded clock error
Assume bounded clock error e
Assume bounded clock error e
http://chess.eecs.berkeley.edu/ptides

## Slide 37: Ptides: Third step: Bind time stamps to real time at sensors and actuators
Input time stamps are ≥ real time
Input time stamps are ≥ real time
Output time stamps are ≤ real time
Output time stamps are ≤ real time
Messages are processed in time-stamp order.
Clock synchronization gives global meaning to time stamps
Actors wrap sensors
Actors wrap actuators
http://chess.eecs.berkeley.edu/ptides

## Slide 38: Ptides: Fourth step: Specify latencies in the model
Global latencies between sensors and actuators become controllable, which enables analysis of system dynamics.
Model includes manipulations of time stamps, which control latencies between sensors and actors
Actuators may be designed to interpret input time stamps as the time at which to take action.
Feedback through the physical world
http://chess.eecs.berkeley.edu/ptides

## Slide 39: Ptides: Fifth step Safe-to-process analysis (ensures determinacy)
Safe-to-process analysis guarantees that the generated code obeys time-stamp semantics (events are processed in time-stamp order), given some assumptions.
Assume bounded network delay d
Assume bounded clock error
Assume bounded clock error e
An earliest event with time stamp t here can be safely merged when real time exceeds t + s + d + e – d2
Assume bounded clock error e
Assume bounded sensor delay s
Application specification of latency d2
http://chess.eecs.berkeley.edu/ptides

## Slide 40: Other Questions about Time:
Precision
  In floating-point formats, precision degrades as magnitude increases
Clear Semantics of Simultaneity
  Requires precise addition and subtraction, e.g. (a + b) + c = a + (b + c). Floating-point numbers don’t have this property.
Floating point numbers are a poor choice for modeling time!

## Slide 41: Topics for further discussion
Programming models leveraging time synchronization?
  PTIDES: http://chess.eecs.berkeley.edu/ptides
How to determine the required accuracy of time sync?
  PTIDES offers a tradeoff between latency and time sync accuracy.
How to handle faults?
  PTIDES can detect violations of assumptions (bounded clock error, bounded network latency, and bounded sensor delay).
Zeno behavior?
  Some models have infinite events in finite time.
Security?
  Does time synchronization create a point of vulnerability? Or does it provide mechanism for improving security? Or both?

## Slide 42: Conclusions
Modeling time as a simple continuum is not adequate.
  Superdense time offers clean semantics for instantaneous events.
Homogeneous time advancing uniformly is not adequate.
  Hierarchical multiform time enables accurate and practical models of heterogeneous distributed systems.
Programming models for distributed cyber-physical systems.
  Ptides is an existence proof that determinate real-time distributed computation is possible.
Floating point numbers for time are not adequate.
  A model with invariant precision and precise addition and subtraction is.
Many more open questions…