## Slide 1
Requirements: Nonvolatility with Low Overheads
  Instantaneous save and restore on power cycles with minimal energy consumption and bandwidth requirements
  Low impact on normal volatile operations
  Hybrid Volatile/Nonvolatile Storage
  Low normal operation penalty
  Explicit nonvolatile store and erase
  Low energy synching
  Compact area
Architecture
Goal: Enable seamless computations on highly energy constrained cyber-physical systems
  Self-powered or battery-limited embedded devices: human body, rural areas, sensor networks, etc.
  Approach: Build nonvolatile microprocessors that preserve state across power interruptions
Benefits: Compute with unreliable power sources; Eliminate virtually all idle power consumption
Nonvolatile Computing
Nonvolatile Computing for Embedded Cyber-Physical Systems
Wing-Kei S. Yu, Shantanu Rajwade, Sarah Q. Xu, Sung-En Wang, Bob Lian, Yu-Yuan Kuo, Edwin C. Kan and G. Edward Suh
School of Electrical and Computer Engineering, Cornell University, Ithaca, NY 14853
Enabling Technology
  Metal nanocrystal Flash
  High endurance
  Relatively low voltage
  Similar technology in production
High-level Operations
  No change to normal operation
  Added NV STORE, NV RESTORE, NV ERASE
Hybrid Memory Cells
Prototype Design
Components designed and simulated on TSMC 0.35µm:
NV SRAM
Charge Pumps and Transmission Gates NV DFF
235,600 µm2
16-bit ultra low-power microcontroller
  TI MSP430 clone (OpenMSP430)
  10MHz, 16 General Purpose Registers (GPR) 128 byte SRAM, 1 KB program Flash
Prototype microcontroller implementation
  Finish full-chip design (analog integration)
  Fabrication and test
On-going Work
Prototype Simulation
OpenMSP430 microcontroller
  Synthesized on TSMC 0.35um with double poly
  Typical standard cell ASIC flow: Synopsys + Cadence
  Standard cell DFFs replaced with our NV version
  Simulated in HSIM with TSMC models and actual layout
Synthesized OpenMSP430
System-level area overhead
  NV area estimate: 2,700,000 um 2 (without program Flash) Volatile only area: 1,276,000 µm2 (without program Flash)
  Overhead can be reduced significantly on an NV compatible process.
NV SRAM
6 transistor baseline
4 extra: 2 NV devices, 2 access devices
NV DFF
22 transistor baseline
4 extra: 2 NV devices, 2 access devices
Restore and Erase operation diagrams
Nonvolatile Cell Operation
Supported by NSF Award CNS-0932069
Other Research Highlights
Hybrid SRAM-DRAM
  Combined SRAM with DRAMs, integrated at cell level
  Enables quick and low energy transfer between the two memory types; increased density vs. SRAM only
  Test circuit was fabricated and tested successfully
Security functions using unmodified Flash memory
  Unique per-device fingerprints
  True quantum random number generation
  Information hiding