## Slide 1: Simple Features and Simple Classifiers for Cyberphysical Systems: Applications to Seizure Detection and Prediction
Keshab K. Parhi
(Joint work with Zisheng Zhang)
Dept. of Electrical & Computer Engineering
University of Minnesota, Minneapolis
Email: parhi@umn.edu

## Slide 2: Outline
Seizure Prediction and Detection Application
Feature Extraction
Feature Ranking
Classification
Low-power and Low-complexity device architecture

## Slide 3
Seizure Prediction Devices
Cyberonics Vagus verve [1]
Neuropace RNS [2]
Medtronic DBS [3]
[1] http://us.cyberonics.com
[2] Two-year seizure reduction in adults with medically intractable partial onset epilepsy treated with responsive neurostimulation: Final results of the RNS System Pivotal trial,” by Heck, C.N., King-Stephens, D., Massey, A.D., Nair, D.R., Jobst, B.C., Barkley, G.L.,…Morrell, M.J., 2014, Epilepsia 55(3), p. 434. Copyright 2014 by Epilepsia.
[3] https://professional.medtronic.com/
Scalp EEG seizure predictor

## Slide 4: Motivation
A patient-specific algorithm that can reliably predict seizures
Low hardware complexity and low power consumption
At least
60 minute gap
Preictal
(Class +1)
Interictal
(Class -1)

## Slide 5: Databases 1 and 2
Freiburg Seizure Prediction Project database
https://epilepsy.uni-freiburg.de/freiburg-seizure-predictionproject/eeg-database
Intracranial EEG (iEEG)
21 patients with medically intractable focal epilepsy
6 electrodes
Sampling frequency: 256 Hz
MIT Physionet EEG database [4]
Scalp EEG (sEEG)
23 patients with intractable seizures
23 bipolar channels
Sampling frequency: 256 Hz
[4] Ali Shoeb. Application of Machine Learning to Epileptic Seizure Onset Detection and Treatment. PhD Thesis, Massachusetts Institute of Technology, September 2009

## Slide 6: Databases 3 and 4
UPenn and Mayo Clinic’s Seizure Detection Challenge database: http://www.kaggle.com/c/seizure-detection
Intracranial EEG (iEEG)
4 canine + 8 human subjects
For dogs
16 electrodes, 400 Hz
For humans
varying number of electrodes, 500 or 5000 Hz
American Epilepsy Society Seizure Prediction Challenge database: http://www.kaggle.com/c/seizure-prediction
Intracranial EEG (iEEG)
5 canine + 2 human subjects
For dogs
16 electrodes, 400 Hz
For humans
varying number of electrodes, 5000 Hz

## Slide 7: PSD Features
Spectral power of signal in a specific band
Relative spectral power of signal in a specific band
Spectral Power ratios between band and band

## Slide 8: Examples of Frequency Band Partition
Sampling frequency: 256 Hz
Band 1: , 4~8Hz
Band 2: 8~13Hz
Band 3: 13~30Hz
Band 4: 30~47Hz
Band 5: 53~70Hz
Band 6: 70~90Hz
Band 7: 90~110 Hz
Band 8: 110~128 Hz
Sampling frequency: 5000 Hz
Band 1: , 4~8Hz
Band 2: 8~13Hz
Band 3: 13~30Hz
Band 4: 30~50Hz
Band 5: 50~80Hz
Band 6: 80~100Hz
Band 7: 100~130 Hz
Band 8: 130~160 Hz
Band 9: 160~200Hz
Band 10: 200~250Hz
Band 11: 250~300Hz
Band 12: 300~350 Hz
Band 13: 350~400 Hz

## Slide 9: Feature Example
Patient No. 1, MIT Database, Scalp electrode 17, /

## Slide 10: Correlation Features
For two r.v. X and Y, correlation coefficient defined as
For n r.v. , defined the element on i-th row and j-th column of the correlation matrix as

## Slide 11: Correlation Matrix (ictal period)
Pat. No. 6, American Epilepsy Society Seizure Prediction Challenge database
Frequency-domain signal
Time-domain signal

## Slide 12: Correlation Matrix (interictal period)
Frequency-domain signal
Time-domain signal
Pat. No. 6, American Epilepsy Society Seizure Prediction Challenge database

## Slide 13: Feature Ranking
F-score
LASSO
Brand and Bound (BAB) + Linear Separability
Classification and Regression Tree (CART)

## Slide 14: Single Feature Selection by F-score
Patient No. 19, MIT, electrode 1, / (good prediction)

## Slide 15: Feature Selection by LASSO
Freiburg, Patient No. 15, electrode 2, prediction
A single spectral power
spectral power versus -to- spectral power ratio

## Slide 16: Feature Selection by BAB
Freiburg, Patient No. 15, electrode 2, prediction
A single spectral power
spectral power versus -to- spectral power ratio

## Slide 17: Feature Selection by CART
patient No. 7, Upenn and Mayo Clinic’s seizure detection contest.

## Slide 18: Cont’d
Electrode 28,
Electrode 27,
Electrode 26,

## Slide 19: Upenn/Mayo Detection Results
Subject name | Feature Details |  |  |  |  | # SZ | SS | AUC
Dog 1 | Electrode | 3 | 8 | 16 |  | 5 | 100 | 0.9773
 | Feature |  |  |  |  |  |  | 
Dog 2 | Electrode | 8 | 7 | 16 |  | 3 | 100 | 0.9975
 | Feature |  |  |  |  |  |  | 
Dog 3 | Electrode | 14 | 7 | 8 |  | 12 | 100 | 0.9876
 | Feature |  |  |  |  |  |  | 
Dog 4 | Electrode | 7 | 8 | 10 | 15 | 2 | 100 | 0.9549
 | Feature |  |  |  |  |  |  | 
Subject name | Feature Details |  |  |  |  | # SZ | SS | AUC
Dog 1 | Electrode | 3 | 8 | 16 |  | 5 | 100 | 0.9773
 | Feature |  |  |  |  |  |  | 
Dog 2 | Electrode | 8 | 7 | 16 |  | 3 | 100 | 0.9975
 | Feature |  |  |  |  |  |  | 
Dog 3 | Electrode | 14 | 7 | 8 |  | 12 | 100 | 0.9876
 | Feature |  |  |  |  |  |  | 
Dog 4 | Electrode | 7 | 8 | 10 | 15 | 2 | 100 | 0.9549
 | Feature |  |  |  |  |  |  | 

## Slide 20
Subject name | Feature Details |  |  |  |  | # SZ | SS | AUC
Pat 1 | Electrode | 19 | 19 | 6 |  | 2 | 100 | 0.9878
 | Feature |  |  |  |  |  |  | 
Pat 2 | Electrode | 1 | 4 | 4 |  | 3 | 100 | 0.9852
 | Feature |  |  |  |  |  |  | 
Pat 3 | Electrode | 5 | 13 | 35 | 9 | 7 | 100 | 0.9506
 | Feature |  |  |  |  |  |  | 
Pat 4 | Electrode | 36 | 36 | 36 |  | 2 | 100 | 1.0000
 | Feature |  |  |  |  |  |  | 
Pat 5 | Electrode | 25 | 13 | 35 | 2 | 3 | 100 | 0.9723
 | Feature |  |  |  |  |  |  | 
Pat 6 | Electrode | 15 | 24 | 16 |  | 4 | 100 | 0.9973
 | Feature |  |  |  |  |  |  | 
Pat 7 | Electrode | 28 | 27 | 26 |  | 3 | 100 | 0.9897
 | Feature |  |  |  |  |  |  | 
Pat 8 | Electrode | 2 | 10 | 17 |  | 4 | 100 | 0.9818
 | Feature |  |  |  |  |  |  | 
Subject name | Feature Details |  |  |  |  | # SZ | SS | AUC
Pat 1 | Electrode | 19 | 19 | 6 |  | 2 | 100 | 0.9878
 | Feature |  |  |  |  |  |  | 
Pat 2 | Electrode | 1 | 4 | 4 |  | 3 | 100 | 0.9852
 | Feature |  |  |  |  |  |  | 
Pat 3 | Electrode | 5 | 13 | 35 | 9 | 7 | 100 | 0.9506
 | Feature |  |  |  |  |  |  | 
Pat 4 | Electrode | 36 | 36 | 36 |  | 2 | 100 | 1.0000
 | Feature |  |  |  |  |  |  | 
Pat 5 | Electrode | 25 | 13 | 35 | 2 | 3 | 100 | 0.9723
 | Feature |  |  |  |  |  |  | 
Pat 6 | Electrode | 15 | 24 | 16 |  | 4 | 100 | 0.9973
 | Feature |  |  |  |  |  |  | 
Pat 7 | Electrode | 28 | 27 | 26 |  | 3 | 100 | 0.9897
 | Feature |  |  |  |  |  |  | 
Pat 8 | Electrode | 2 | 10 | 17 |  | 4 | 100 | 0.9818
 | Feature |  |  |  |  |  |  | 
Cont’d

## Slide 21: Feature Selection by CART
Dog 2, American Epilepsy Society Seizure Prediction Challenge database
electrode importance

## Slide 22: Upenn/Mayo Prediction Results
Subject name | Comparison |  |  |  |  |  |  |  | # SZ
 | Electrodes No. |  | # Features |  | Classifier |  | AUC |  | 
 | baseline | proposed | baseline | proposed | baseline | proposed | baseline | proposed | 
Dog 1 | 1 3 5 8 11 | 1 3 5 8 11 | 275 | 50 | RBF-SVM | Polynomial-SVM (d=4) | 0.9975 | 0.9934 | 4
Dog 2 | 9 11 12 15 | 9 11 12 15 | 220 | 50 | RBF-SVM | Polynomial-SVM (d=4) | 1.0000 | 0.9987 | 7
Dog 3 | 7 9 10 15 | 7 9 10 15 | 220 | 50 | RBF-SVM | Polynomial-SVM (d=4) | 0.9978 | 0.9333 | 12
Dog 4 | 3 6 7 | 3 6 7 | 155 | 35 | RBF-SVM | Polynomial-SVM (d=4) | 0.9984 | 0.9542 | 17
Dog 5 | 12 13 14 | 12 13 14 | 155 | 20 | RBF-SVM | Polynomial-SVM (d=4) | 0.9961 | 0.9698 | 5
Pat .1 | 2 13 15 | 2 13 15 | 234 | 20 | RBF-SVM | Polynomial-SVM (d=4) | 1.0000 | 1.0000 | 3
Pat. 2 | 1 12 14 | 1 12 14 | 234 | 20 | RBF-SVM | Polynomial-SVM (d=4) | 1.0000 | 1.0000 | 3

## Slide 23: Cont’d
Vdd(V) |  |  | Energy(pJ) w opt | Energy(pJ) w/o opt | Frequency
Linear |  |  |  |  | 
1.0 |  | 32 64 128 | 49.1 81.8 147.3 | 70.92 118.2 212.76 | 10M Hz
2nd order Polynomial |  |  |  |  | 
1.0 |  | 32 64 128 | 1570.6 5235.2 18847.14 | 2269.44 7564.8 27223.28 | 10M Hz
Vdd(V) |  |  | Energy(pJ) w opt | Energy(pJ) w/o opt | Kernel
1.0 | 100 | 64 | 81.8 5235.2 10633.61 | 118.2 7564.8 15523.67 | Linear Poly RBF
Vdd(V) |  |  | Energy(pJ) w opt | Energy(pJ) w/o opt | Frequency
Linear |  |  |  |  | 
1.0 |  | 32 64 128 | 49.1 81.8 147.3 | 70.92 118.2 212.76 | 10M Hz
2nd order Polynomial |  |  |  |  | 
1.0 |  | 32 64 128 | 1570.6 5235.2 18847.14 | 2269.44 7564.8 27223.28 | 10M Hz
Vdd(V) |  |  | Energy(pJ) w opt | Energy(pJ) w/o opt | Kernel
1.0 | 100 | 64 | 81.8 5235.2 10633.61 | 118.2 7564.8 15523.67 | Linear Poly RBF

## Slide 24: Decision Variables
Dog 2, American Epilepsy Society Seizure Prediction Challenge database
Human 2, American Epilepsy Society Seizure Prediction Challenge database

## Slide 25: Conclusion
In power-constrained CPS, feature selection is an important step
Simple classifiers with few features can achieve higher sensitivity/specificity than many features and the most powerful classifier
Low-Power architectures for a clinically acceptable seizure prediction system relies on selection of few features and simple classifiers