## Slide 1: META II: EPS Steady State Analysis Tool
META II - Task 1: Alessandro Pinto, Fernando Rodriguez, and John Finn
Delivered to the U.S. Government in Accordance with Contract FA8650-10-C-7080.
(c) 2011 United Technologies Corp.
Developed with the sponsorship of the Defense Advanced Research Projects Agency (DARPA).
Permission is hereby granted, free of charge, to any person obtaining a copy of this data, including any software or models in source or binary form, as well as any drawings, specifications, and documentation (collectively "the Data"), to deal in the Data without restriction, including without limitation the rights to use, copy, modify, merge, publish, distribute, sublicense, and/or sell copies of the Data, and to permit persons to whom the Data is furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all copies or substantial portions of the Data.
THE DATA IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE AUTHORS, SPONSORS, DEVELOPERS, CONTRIBUTORS, OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM, OUT OF OR IN CONNECTION WITH THE DATA OR THE USE OR OTHER DEALINGS IN THE DATA.

## Slide 2: EPS Steady State Analysis Tool Description
An EPS topology is a circuit network connecting sources and loads. Load powers are known rather than impedances which results in network equations in terms of power known as power flow equations. Power flow equations are complex nonlinear algebraic equations, therefore they must be solved by iterative methods. A set of equations (1) & (2) are written for each bus in a topology. The equations are coupled through the admittance vales (Yij) and their solution yields the power and voltage at each node.
Where,

## Slide 3: EPS Sample Topology
Bus No | Load Index | Load Description | Power (kVA) | PF
E_B3 | Load_1 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_3 | Fuel Pump (FP) | 6 | 0.97
 | Load_5 | Avionics (A) | 2.56 | 0.97
 | Load_7 | Ice/Rain proctection (IRP) | 2.6 | 0.97
 | Load_9 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_11 | Fuel boost pump (FBP) | 7.04 | 0.9
E_B4 | Load_13 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_15 | Window Heat (WH) | 0.8 | 0.97
E_B11 | Load_17 | DC Load | 6.08 | 1
B7 | Load_19 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_21 | Fuel Pump (FP) | 6 | 0.97
 | Load_23 | Avionics (A) | 2.56 | 0.97
 | Load_25 | Ice/Rain protection (IRP) | 2.6 | 0.97
 | Load_27 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_29 | Fuel boost pump (FBP) | 7.04 | 0.9
B8 | Load_31 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_33 | Window Heat (WH) | 0.8 | 0.97
B13 | Load_35 | DC Load | 6.08 | 1
E_B5 | Load_2 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_4 | Fuel Pump (FP) | 6 | 0.97
 | Load_6 | Avionics (A) | 2.56 | 0.97
 | Load_8 | Ice/Rain protection (IRP) | 2.6 | 0.97
 | Load_10 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_12 | Fuel boost pump (FBP) | 7.04 | 0.9
E_B6 | Load_14 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_16 | Window Heat (WH) | 0.8 | 0.97
E_B12 | Load_18 | DC Load | 6.08 | 1
B9 | Load_20 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_22 | Fuel Pump (FP) | 6 | 0.97
 | Load_24 | Avionics (A) | 2.56 | 0.97
 | Load_26 | Ice/Rain proctection (IRP) | 2.6 | 0.97
 | Load_28 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_30 | Fuel boost pump (FBP) | 7.04 | 0.9
B10 | Load_32 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_34 | Window Heat (WH) | 0.8 | 0.97
B14 | Load_36 | DC Load | 6.08 | 1
The 36-load list was used to create a sample EPS topology in order to develop and test the evaluation tool. A detailed Netlist is created to describe the complete topology consisting of 3 Sources, 4 Converters, 58 Switches, 36 Loads, 66Transmission lines and +100 nodes. Converters are currently bypassed by modeling DC loads with AC equivalent (PF=1).

## Slide 4: EPS Sample Topology
The detailed EPS topology shows the interconnections for all source, loads, switches, and transmission lines. The diagram is used to create a topology Netlist which is fed to the steady state analysis tool.
Switches throughout the network can be turned -OFF by setting their value to zero in the Netlist.
For example, if the EPS topology is to be evaluated without Load 1, then Switch 8 should be set to zero.

## Slide 5: EPS Sample Topology - Netlist
Input: Netlist
Source_data = [(Bus No) (Bus Code) (EPS Code) (real power) (reactive power)]
SW_data = [ (SW No) (EPS Code) (node 1) (node 2) (Impedance)]
SW_Z =generic switch impedance in ohms per phase @ 400Hz
SW = row vector for all switches (1 = ON, 0 = OFF)
TL_data = [ (TL No) (EPS Code) (node 1) (node 2) (Impedance)]
TL_Z = generic switch impedance in ohms/ft per phase @ 400Hz
TL = row vector for all transmission paths lengths specified in feet.
Conv_data = [ (Conv No) (Bus in) (Bus out) (EPS Code IN) (EPS Code OUT) (Conv eff)]
Load_data = [ (Bus No) (Bus Code) (EPS Code) (real power) (reactive power) ]
EPS_Code = [ (EPS Code No) (DC=1/AC=2) (Vm) (No. of Phases)]
------------------------------------------------------------------------------------------------------------------------------------------------
Output
Power Flow = [ (Bus No) (Vm) (Angle) (Pd) (Qd) (Pg) (Qg)]
To run the sample EPS topology analysis, open and run EPS_Load_Flow.m. Additional files needed to run the SS analysis include topologyRev03_36L.m, Graph_reduction.m, reorder.m, EPSdata_process.m, lfybus.m, lfnewton.m, busoutprep.m, and busout.m.

## Slide 6: Setting switches to OFF state - Netlist
A screen capture of the Netlist shows how switches can be turned OFF. Setting the switch to zero (SW(#) =0) opens the switch.
Switches 3, 5, 30, 32, 26, 27, 56, 54, 58, & 53 are OFF.
Netlist: Switch Data