## Slide 1: META II: EPS Dynamics Analysis Tool
META II - Task 1: Alessandro Pinto, Fernando Rodriguez, and John Finn
Delivered to the U.S. Government in Accordance with Contract FA8650-10-C-7080.
(c) 2011 United Technologies Corp.
Developed with the sponsorship of the Defense Advanced Research Projects Agency (DARPA).
Permission is hereby granted, free of charge, to any person obtaining a copy of this data, including any software or models in source or binary form, as well as any drawings, specifications, and documentation (collectively "the Data"), to deal in the Data without restriction, including without limitation the rights to use, copy, modify, merge, publish, distribute, sublicense, and/or sell copies of the Data, and to permit persons to whom the Data is furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all copies or substantial portions of the Data.
THE DATA IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE AUTHORS, SPONSORS, DEVELOPERS, CONTRIBUTORS, OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM, OUT OF OR IN CONNECTION WITH THE DATA OR THE USE OR OTHER DEALINGS IN THE DATA.

## Slide 2: EPS Dynamics Analysis Tool Description
Five script/simulation files carry out the dynamic simulation
  Set simulation parameters (runsim_c.m)
  EPS Netlist (topologyRev03_xxL.m)
  State space formulation (statespace_formulation_rev08_orig.m)
  State space simulation (solverABCD_man_file_C_feed.mdl)
  Plot Bus Voltage vs Time results (plot_data.m)
Sample topology was created as a test case
  Topology loosely based on B-777 topology
  36 loads total a max load capacity of ~186kVA
Dynamics in an EPS can occur due to sudden changes in load, faults, switch actuation, etc. During a transient response, bus voltages must remain within pre-defined limits. An analysis tool is being developed which will accept an EPS Netlist and automatically generate its state space model. MATLAB is the development platform and the tool is described below:

## Slide 3: EPS Sample Topology Simulations
Bus No | Load Index | Load Description | Power (kVA) | PF
E_B3 | Load_1 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_3 | Fuel Pump (FP) | 6 | 0.97
 | Load_5 | Avionics (A) | 2.56 | 0.97
 | Load_7 | Ice/Rain proctection (IRP) | 2.6 | 0.97
 | Load_9 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_11 | Fuel boost pump (FBP) | 7.04 | 0.9
E_B4 | Load_13 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_15 | Window Heat (WH) | 0.8 | 0.97
E_B11 | Load_17 | DC Load | 6.08 | 1
B7 | Load_19 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_21 | Fuel Pump (FP) | 6 | 0.97
 | Load_23 | Avionics (A) | 2.56 | 0.97
 | Load_25 | Ice/Rain protection (IRP) | 2.6 | 0.97
 | Load_27 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_29 | Fuel boost pump (FBP) | 7.04 | 0.9
B8 | Load_31 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_33 | Window Heat (WH) | 0.8 | 0.97
B13 | Load_35 | DC Load | 6.08 | 1
E_B5 | Load_2 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_4 | Fuel Pump (FP) | 6 | 0.97
 | Load_6 | Avionics (A) | 2.56 | 0.97
 | Load_8 | Ice/Rain protection (IRP) | 2.6 | 0.97
 | Load_10 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_12 | Fuel boost pump (FBP) | 7.04 | 0.9
E_B6 | Load_14 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_16 | Window Heat (WH) | 0.8 | 0.97
E_B12 | Load_18 | DC Load | 6.08 | 1
B9 | Load_20 | Navigation Lights (NL) | 2.56 | 0.97
 | Load_22 | Fuel Pump (FP) | 6 | 0.97
 | Load_24 | Avionics (A) | 2.56 | 0.97
 | Load_26 | Ice/Rain proctection (IRP) | 2.6 | 0.97
 | Load_28 | Equipment Cooling Fan (ECF) | 4.64 | 0.9
 | Load_30 | Fuel boost pump (FBP) | 7.04 | 0.9
B10 | Load_32 | Hydraulic pump (HP) | 14.24 | 0.9
 | Load_34 | Window Heat (WH) | 0.8 | 0.97
B14 | Load_36 | DC Load | 6.08 | 1
All EPS components are modeled with inductor-resistive models. The load list table describes how the loads are connected to the EPS buses. The state space simulation reveals the instantaneous bus voltages during transient events.

## Slide 4: EPS Sample Topology Simulation Results
The simulation results display the Voltage vs Time plots for the EPS buses during a system start-up. For this particular simulation all loads are power by G1. Further development is in process to dynamically recalculate the state-space to model multiple generators and switch actuation. The voltage numbers can be mapped to the detailed EPS Netlist graph in the following slide. A more concise simulation tool is also in development which will allow for easier bus voltage requirement verification.

## Slide 5: EPS Sample Topology - Netlist Graph

## Slide 6: How to run a simulation files
To run the EPS dynamic simulation open and run the script file (runsim_C.m). The simulation may take up to ~1min to execute: bus voltages and load current plots will be generated automatically.