## Slide 1: RLC Toy Problem: Design Methodology
Alessandro Pinto
alessandro.pinto@utrc.utc.com
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAAA
UTC Proprietary - This material contains proprietary information of United Technologies Corporation. Any copying, distribution, or
dissemination of the contents of this material is strictly prohibited and may be unlawful without the express written permission of UTC.
If you have obtained this material in error, please notify UTRC Counsel at (860) 610-7948 immediately.

## Slide 2: Main message
Filter design
Layout
Filter design
Filter design
Layout
Packaging and Thermal
Prototype and Test
Filter design
Layout
Packaging and Thermal
Prototype and Test
Traditional flow
Proposed methodology
Notes: Traditional design flow is typically layered
Filter design. Given the frequency response, find the topology and the values of the components.
Given the components and a constraint on size, find position of each component (connections are also established)
Packaging and thermal analysis. The board is packaged and thermal analysis is carried out
Prototype and test. The circuit is built and assembled. Tests are performed to check if the circuit satisfies the original specification
Any problem found in during the prototype and test phase may lead to a re-design cycles. The most expensive ones are the ones that trace back to the filter design state. In this case, the prototype needs to be rebuilt and test needs to be performed again. Moreover, the design flow is not formally connected through models. For example, the packaging and thermal analysis might be performed only to check that some temperature bounds are met or that power is evenly distributed. However, most of the constraints taken into account during filter design (such as bandwidth) are not checked.
The proposed design flow relies on some unique features:
-Some models and constraints are abstracted from the lowest level of abstract to the highest. This means that during filter design some packaging and layout constraints are taken into account, limiting the need for redesign cycles.
-The different views are always kept together so that the original specification of the system (in this case the bandwidth and Q factor) are continuously checked even in the later stages of the analysis.
-Validity of models can be also checked as will be clear later in this presentation.

## Slide 3: The filter design stage
Consider the topology given
We will use the notion of contracts (a pair of assumption and guarantee described as constraints on variables)
  Contracts can be composed and checked for refinement
Electrical contract
Layout contract
Thermal contract
EMI contract
Specification
Variables: vi, vo, R, L, C, i, Tc, dist, conv, n
Layout
Thermal
EMI
Notes: We are at the point where the topology of the filter is given (e.g. the one given by DARPA).
We will use now contracts to define formally our problem. We will have several types of contracts already at the filter design level. This is necessary to consider the interactions among physical quantities. These contracts can also be “empty” meaning that the interactions might be considered weak and therefore uninteresting at this level.
The specification of what the system is expected to do is also captured as a contract.
Contracts are constraints (some are assumptions and some are guarantees). These constraints are defined on variables. We consider the input voltage v_i, the output voltage v_0, the current i, the parameters of the circuit R, L and C, a distance parameter dist, a convective coefficient parameter conv, and a noise parameter n.

## Slide 4: Specification contract – Example
If this contracts are made probabilistic (by specifying a probability that the guarantee be satisfied), then we allow for some yield, meaning some boards are going to be discarded (but still no need to re-design, we allow this in the specification).
Specification
A:
G:
A:
G:
C1
C2
(Cut-off frequency)
(Noise level at different tones)
Notes: Each contract can actually be broken down into several contracts that must all be satisfied. The actual contract is then the conjunction. Here we show two contracts: one on the cut-off frequency of the filter, and one on the maximum rms level of noise for sinusoidal inputs.
Notice that contract C_1 does not specify any particular input waveform which makes simulation an ineffective method to analyze this system.

## Slide 5: Electrical contract – Example
A:
G:
C3
(Any environment)
A:
G:
C4
A:
G:
C6
A:
G:
C5
Electrical contract

## Slide 6: Thermal contract – Example
Thermal contract
A:
G:
C7
EMI contract
A:
G:
C8

## Slide 7: Filter design
Contracts must be all compatible
  In particular the original specification must be satisfied
In this case the design is reduced to determining dist and conv
If R, L and C are not given, then those variables are also part of the design.
Dist will become a constraint for the layout and conv for the packaging as well
Notice that C6, C7, C8 are very abstract models but we will keep them in the system to check at the lower levels that they are satisfied; if not, then a flag is raised

## Slide 8: Layout
This is a design exploration problem
  Library
  Composition rules
  Specification (comes from the previous step, dist · x)
  Metrics (could be minimum space or no metrics)
Variables: ¢, ½, x1, y1, … xn, yn
Position of pins
( x1 , y1 )
( x2 , y2 )
A:
G:
Cl,1
Description of a typical n-pin component
2-pin component

## Slide 9: Platform and specification
Components
Rules
A:
G:
Cp,1
Platform
Specification

## Slide 10: Layout problem
Given the constraints from the platform and from the specification, find position of first pin, translation and orientation.
Once solved, the layout view is added to the components and can be used later in the thermal analysis.

## Slide 11: Packaging and thermal analysis
Electrical contract
Layout contract
Thermal contract
EMI contract
Specification
Detailed thermal contract
·