## Slide 1
Promise: Military-Relevant Models and Case Studies and Findings on Compositionality
DARPA META PI Meeting – Jan 12-13, 2011
Grit Denker, Linda Briesemeister, Daniel Elenius, Shalini Ghosh, Minyoung Kim, Mark-Oliver Stehr, Ashish Tiwari (SRI International)
Devesh Bhatt, Siamak Nikbin, Haftay Hailu (Honeywell Aerospace Advanced Technology)
Xenofon Koutsoukos (Vanderbilt University)
Guenther Bauer, Martin Schwarz, Wilfried Steiner (TTTech Computertechnik AG)

## Slide 2: Overview
Military-Relevant Models and Case Studies
  Dual Cabin Air Compressor (CAC) Subsystem
  Component Failures, Detection and Relationships
  Compositional Aspects of Verification
Findings on Compositionality
  Compositional Reasoning on PI Controllers (-> Demo)
Verification Approaches and Tools Overview
Findings on Compositionality
  Fault Analysis using Probabilistic Inference (-> Demo)
Integration with Vanderbilt META Language and Design Flow
  HybridSAL Integration
Sources of Probability
Compositionality Challenges

## Slide 3: Military-Relevant Models and Case Studies

## Slide 4: Case Study – “More Electric” Environmental Control System (ECS)
Purpose of Case Study
  Provide examples of verification requirements to exercise generic tool capabilities
  A mix of different types of components and verification aspects
    Software, electro-mechanical, pneumatic components
    Hybrid control
    A mix of scenarios of failures and degraded modes of operation
Incremental approach to case study development
  Start with inner part of the ECS architecture
    Dual Cabin Air Compressor (CAC): Inner-loop controls and supervisory modes
    Failure modes, probabilistic analysis
  Add higher-level operational modes/scenarios and component interactions
    Examples for compositional verification
    Examples for multi-dimensional design trade-off analysis (MD-TA)
  Extend to aircraft level integration case study:
    Coupling and “emergent behavior”: network, power, thermal, ducts
  Verification objectives in the case study should have generic applicability

## Slide 5: “More Electric” Environmental Control System (ECS) Architecture
Dual Cabin Air Compressor (CAC) subsystem

## Slide 6: Dual CAC System: Physical Architecture
Aircraft
Motor power
CAN BUS
Sensor signal
System Controller
(SC)
Motor Controller 1 (MC)
CAN Bus 1
CAN Bus 2
Motor Controller 2 (MC)

## Slide 7: Dual CAC System: Control functions
CAC1 PI Control
CAC2 PI Control
Motor Contr 2
Supervisory Mode Control
Plant
feedback
Aircraft
Set Point Selection
Plant
ECS_Start
Altitude
ADS_Mode
Motor
Contr 1
Fail, RPM

## Slide 8: Component Failures, Detection, Relationships
Component | Failure Type | Detection | Effects, Mitigation, Relationships
CAN Bus | Message loss | SC detects | If message loss to one CAC then shut that down. If both CACs unreachable then system fail. CAN Bus failures are temporary => bring back online within flight.
Motor Controller | Overheating (Temp sensor) | MC detects, notifies SC | Cooling system design tradeoff – single cooling control (weighted average of temp) vs. independent controls. Increased load on cooling system => increased probability of other failures
 | Contactor failure | MC detects, notifies SC | Motor shutdown, increase load (flow) of other CAC => increased probability of other CAC failure with time
Motor | Overheating | MC detects, notifies SC | Similar to above.
 | Stalling | MC detects, notifies SC | Temporary motor shutdown, attempt to bring back on line within flight.
Turbomach./ Compressor | Overheating | MC detects, notifies SC | Similar to above.
Flow Sensor | Reading outside range limits | SC detects | Control design tradeoff – use other flow sensor and apply same speed to both CACs vs. accommodate for changes in flow from the two CACs (also, manufacturing artifacts)

## Slide 9: Aircraft Level Network / Compositional Aspects of Verification
Mixed mode TTEthernet
Mix of Rate Constrained (RC), Time Triggered(TT) traffic combined with physical aspects
  Hierarchy of buses (aircraft network and SC network etc.) vs single network
    Put all traffic on one network, but assign different priorities to traffic classes
    Fault tolerance alternatives: serial redundancy to control failure, use of self-checking pair
    Compare benefits/shortcomings of single vs multiple network architectures
  Replace CAN Bus with TTEthernet, prove that TTEthernet satisfies CANBus guarantees; then compose with other applications
    Physical distribution of component (e.g., redundant components or sensors) is linked to communication delay
Verification to Enable Design Trade-off and Composition
  Design (control/physical) choices to mitigate impact of failures
    Temporal aspects of conditional failures/probabilities
  Verify that variations of component designs meet certain properties when composed
    “optimal” designs and compositions that are verifiable
  Effect of thermal/cooling coupling at the aircraft level
    E.g.: Discretized models (e.g., temperature = {very hot, hot, …} & conditional probabilities about dependent failures relative to temperature)

## Slide 10: Findings on Compositionality
Compositional Reasoning on PI Controllers

## Slide 11: Motivation
All complex cyber-physical systems (CPS) will have a controller module.
PI (proportional-integral) controllers are the most often used feedback controllers in industrial control systems.
  Motor controller in the CAC case study is a PI controller.
Motivating Question
If a PI controller were available as a component module in a library, how would we reason about it and determine if its composition with other components results in a safe system?

## Slide 12: PI Controller as a Component
A typical control system:
PI Controller
Plant
U
X
PI Controller
Plant
X
U
X
U
A compositional view:
PI controller takes x as input, produces u as output
Plant takes u as input, produces x as output
How to reason compositionally?

## Slide 13: Assume-Guarantee Reasoning
Assume-Guarantee is a classical approach for performing compositional reasoning.
Each component comes with contracts:
  Assumptions: What do I assume about my environment?
  Guarantee: If the assumption I make about my environment holds, what guarantee do I give?
When composing subsystems A and B, one needs to verify that the assumptions made by A are satisfied by the guarantees generated by B, and B's assumptions are satisfied by the guarantees generated by A.

## Slide 14: Assume-Guarantee Pair for PI Controller
Assumption: The plant responds to the control input.
  Formally, the PI controller assumes that the output x of the plant changes in response to the control input u as follows
    dx/dt = -alpha*u
  where alpha is lower-bounded by a positive number.
Guarantee: The PI controller guarantees that the error always eventually drops below a fixed constant.
  Formally, in temporal logic,
    G (F ( error <= 1 ) )
Compositionality Theorem:
  If the plant satisfies the assumption made by the PI controller, then the PI controller will ensure the composed system satisfies the guarantee.

## Slide 15: Discovering and Proving the Compositionality Theorem
The key ideas behind our technical approach are
Constraint-based Verification
  We perform verification by discovering "certificates of correctness”.
  These certificates take the form of
    Lyapunov functions for stability verification
    Inductive invariants for safety verification
Real Quantifier Elimination
  The verification engineer fixes a form of the certificate.
    V := c * error^2 + d * interr^2
  Suitable values for c and d are found using modern real quantifier elimination engines
  Examples of such tools include
    Quantifier Elimination by Partial Cylindrical Algebraic Decomposition (qepcad - http://www.usna.edu/Users/cs/qepcad/B/QEPCAD.html)
    Reduce logic system (redlog - http://redlog.dolzmann.de/)

## Slide 16: Technical Statement of the Compositionality Theorem for PI Controllers
Consider any PI controller that satisfies these two assumptions:
the proportional gain is larger than the integral gain:
  Kp >= Ki
the integral of the error term is saturated
Then, this controller when composed with any plant that satisfies
  dx/dt = -alpha*u
  where alpha can non-deterministically vary as long as it is lower-bounded by a positive quantity
will guarantee that the error term will eventually drop below the constant 1.
The restrictions on the PI controllers are required; without them the proof fails.
Demo

## Slide 17: Verification Approaches and Tools Overview

## Slide 18
Property Complexity
System (Model) Complexity
Partial
Information
Type Correctness
Ranges
Safety/
Reachability
Stability
Probabilistic
Full Correctness
Finite
State
Infinite
State
Discrete
Hybrid
Stochastic
Networked
CPS
Model Checkers, Abstractors
Constraint-Based Verification
Stochastic Model Checkers
Extended Type Checkers
Type Checkers,
Static Analyzers
Probabilistic Model Checkers & Inference
Theorem Provers
Testing
Infinite Bounded Model Checkers
Code Review
Notes: sum-of-squares tools (CalTech control theory group) - Numerical approach, rather than symbolic, for proving theorems over the reals- use convex optimization - popular for finding Lyapunov functions of control systems

## Slide 19
Property Complexity
System (Model) Complexity
Partial
Information
Type Correctness
Ranges
Safety/
Reachability
Stability
Probabilistic
Full Correctness
Finite
State
Infinite
State
Discrete
Hybrid
Stochastic
Networked
CPS
Model Checkers, Abstractors:
SAL, HybridSAL, PHAVer, Uppal
Constraint-Based Verification:
SOS Tools, HybridSAL
Stochastic Model Checkers:
PRISM
Extended Type Checkers:
HiLiTE
Type Checkers,
Static Analyzers: Astree
Probabilistic Model Checkers & Inference
Theorem Provers:
PVS, Coq, ACL2
Testing:
MATLAB/Simulink
Infinite Bounded Model Checkers:
SAL
Code Review
Notes: sum-of-squares tools (CalTech control theory group) - Numerical approach, rather than symbolic, for proving theorems over the reals- use convex optimization - popular for finding Lyapunov functions of control systems

## Slide 20: Findings on Compositionality
Fault Analysis Using Probabilistic Inference

## Slide 21: Fault Analysis in Avionics
Traditional approach
  Perform both FTA (Fault Tree Analysis) and FMEA (Failure Modes and Effects Analysis), with a failure mode effects summary (FMES) as the interface between FMEA and FTA.
    FTA: is a deductive, top-down method aimed at analyzing the effects of initiating faults and events on a complex system.
        undesired system state is analyzed using boolean logic to combine a series of lower-level events.
    FMEA: is an inductive, bottom-up analysis method aimed at analyzing the effects of single component or function failures on equipment or sub-systems.
Newer approaches
  Fault Propagation and Transformation Calculus (FPTC)
    Modular representation and compositional analysis of hw & sw components
  Hierarchically Performed Hazard Origin and Propagation Studies (HiP-HOPS)
    Manually model system and annotate failures; automatically generate FTA and FMEA
  Probabilistic Failure Propagation and Transformation Analysis (FPTA) using PRISM
  Markov analysis: Probabilistic fault modeling to infer the probability of an undesired event using SRI’s Probabilistic Consistency Engine

## Slide 22: Probabilistic Consistency Engine (PCE) Basics
PCE is a tool developed at SRI for doing probabilistic inference
  Based on the theory of Markov Logic Networks (MLNs)
  It draws on the work of Pedro Domingos et al. and the Alchemy system
PCE can infer the marginal probabilities of formulas based on probabilistic facts and rules
  Facts and rules are presented in an order-sorted first-order logic
  Each fact and rule can have an associated prior probability/weight
  The PCE input language consists of sorts, subsorts, constants, observable/direct predicates and hidden/indirect predicates, and weighted facts and rules
Inference is carried out using a scalable sampling-based method
  The MCSAT inference averages the probabilities over a sequence of random models generated using SampleSAT
PCE is general enough to capture many other graph-based formalisms for probabilistic reasoning

## Slide 23: Fault Analysis Methodology Using PCE
Component Model
Component Model
Component Failure Probabilities
e.g., from library
Component and System-Level Failure Model
Modeled as (conditional) prob. rules
Incl. failure relationships
Uses: Subject Matter Expert (SME) knowledge, historic data
System Architecture
Component Model
Component Model
Component Model
Modeled as facts
Needs: SME input, measurements
Probabilistic Inference
(Sub)System Failure Probability
Forward and Reverse Analysis
Infer probability of system failure given component failure probabilities
Infer requirements on component failure probabilities for given system failure threshold
Redo inference with various component failure probabilities
until desired system failure probability is reached or
to determine effect on system failure probability

## Slide 24: New Paradigms in Fault Analysis
Capture the failure probabilities of the component and subcomponents in a system in terms of probabilistic first order logic (FOL) relations
  More expressive; probabilities/weights on the FOL rules allows reasoning with uncertainty.
Go beyond i.i.d. (independently and identically distributed) assumptions in fault-tolerance and model failures using conditionals
  The i.i.d. assumptions used commonly in probabilistic analysis of faults are often not realistic in many domains.
  Example: If one CAC fails, then there is higher load on the second CAC, thus second CAC has higher probability of failure.
  Already incorporated conditionals into PCE fault models, which seems to give reasonable results; need to do more complex models in the future
Experiment with new concepts like "timeline-of-failures”
  Need to incorporate temporal reasoning into PCE models – "time" as a variable in the PCE model along with temporal rules/constraints.
Demo

## Slide 25: Integration with Vanderbilt META Language and Design Flow

## Slide 26: Integrating HybridSAL
System specification in CyPhy
  Physical components: Bond Graph language
  Cyber components: ESMoL
  Interconnections: Architecture language
Model transformation to MATLAB Simulink/Stateflow
Model transformation to hybrid automaton
Properties to be verified: Requirements language
  LTL formulae
HybridSAL verification
Valuation of the safety properties in the Requirements model
HybridSAL
GME Models
DESERT
Requirements
Bond Graph
ESMOL
Architecture
Simulink/ Stateflow

## Slide 27: Translation of MATLAB Simulink/Stateflow Models to Hybrid Automata
Input: A subset of MATLAB Simulink/Stateflow
Output: Hybrid automaton in HybridSAL
Semantic interoperability
Graph Rewriting and Transformation (GReAT) language
  Metamodel-based graph transformation tool

## Slide 28: Sources of Probability

## Slide 29: Sources of Probability I
Input data
  Probabilities of input data. E.g.,
    component failure and failure modes probabilities
    traffic profile probabilities
    performance probabilities (e.g., communication latencies)
  Conditional probabilities of input data
  Distribution of ranges of input data
  Expected time of arrival of input data
Environment disturbances/uncertainties/noises
State-dependent probabilities
  Probability as function of time, temperature or other attributes
  E.g.,
    Mean time between failures of components
    Conditional probabilities (failing of one component increasing likelihood of another component failure)

## Slide 30: Sources of Probability II
Confidence in/realism of model
  Related to abstraction level used for modeling
  Probabilities coming from design parameter probability distribution (acquired in design simulation phase of higher fidelity models)
Probabilistic verification results
  Sampling/simulation deliver probabilities/confidence intervals
  Raises question about how probabilities are propagated in composition framework (across proofs)
  Even if verification results are 100% proofs (e.g., model checkers like HybridSAL), counterexamples could be interpreted as probability of failure in concrete model
  State estimation problem / Model-based diagnosis: Output of tools is probabilistic
Scalability limit of model/tools
  Problem: Can this be quantified?
Qualification of tools
  Bugs in tools
  Verification of tool results

## Slide 31: Compositionality Challenges

## Slide 32: Compositionality Challenges
Composing Models
  expressiveness of modeling language
  choice of composition operators
Composing Properties
  expressiveness of property language
    Example properties: safety, liveness (stability), interference freedom
  style of compositionality theorems
    E.g., assume/guarantee
  each composition operator can have multiple associated theorems
Composing Proofs
  proof representation language
  proof composition as a function of component proofs
  each compositionality theorem has underlying proof composition function
Heterogeneous Proofs
  heterogeneity of modeling/property languages
  compose results from different proof tools
Multi-dimensional Composition
  multiple perspectives and abstractions
  capture and exploit relations between models
Probabilistic Certificates as a Generalization of Proofs
  atomic certificates to represent output of tools
  flow of probabilities along the composition hierarchy

## Slide 33
Thank You