## Slide 1: PROMISE Verification of multi-component integrated control functions using HiLiTE and other PROMISE Tools v6 4/25/11
PROMISE Team

## Slide 2: Motivation and Context
Verification of Integration of Control Function Components (e.g., flight controls)
  Flight control – several “partitions” of control functionality
    Primary Flight, High Lift, Auto Flight
  Each partition has multiple models – total of ~2000 models, ~4-5 M SLOC
    Each model is a “sub component” that implements specific system level requirements
      Requirements and corresponding models are managed/tuned quasi-independently
    System environment assumptions: scheduling of models on processor and cross-lane comparison of intermediate results from dissimilar processors
  The problem:
  When the components are integrated – computations in a component influence correctness of certain properties of control algorithm in a downstream component. Certain aspects of the correctness of each component need to be verified within the integrated system.
    Not all verification “assumptions” of a component (inputs, environment) can be a priori specified – e.g. enormous combinations of input constraints that can yield guarantees
    Certain “guarantees” can be regarding the correctness of internal states of components: such as required range bounds on internal variables and temporal constraints (e.g., rate bounds)
      Other guarantees: regarding bounds on outputs of components feeding to other components
      a priori assertions in each model as a condition of reuse
    Even though component designs (models) and code can be parameterized and reused across aircraft configurations, “verification must be re-done on exact bounds/constraints of the parameters in a set of integrated components for a specific configuration”. The space of all interactions of generic parameter bounds of multiple components is not well understood.

## Slide 3
Computation of intermediate ranges (and other constraints) between models
  Determine order of execution of models and sources of external inputs in a partition
  Run HiLiTE on multiple (200 - 1200) models in a partition
  Multiple runs until all computed ranges stabilize (feedback paths between models)
    If the ranges do not stabilize after a certain number of iterations then there is divergent feedback – a design problem – this has been tried
    Depends upon the cross-aspect assumptions of scheduling and cross-lane comparisons
  HiLiTE computes range bounds for intermediate signals and model outputs
  HiLiTE checks properties: e.g., overflows, bounds required, specific “design defects”
Extend Vanderbilt GME-based tool
  capture interfaces/interconnection of models
  interface properties such as ranges and other properties to be checked
  Tool also generates scripts/command files to run HiLiTE on the models
  Annotate back results of analysis and verification anomalies found.
Simulink
Model1
Rate = x
Model2
Model3
computed
outgoing ranges
to external sources
incoming ranges
from external
Sources
(other partitions, system dictionaries, aircraft I/O - A/D)
Intermediate signals’
ranges computed
One
Partition
Approach

## Slide 4
Phase 1: Perform “Forward propagation” and checking of properties across multiple models
  Initial extended tool to capture models, interconnections, and ranges
  Abstracted control algorithm models
Phase 2: Mapping to Assume/Guarantee Clauses
  Backwards propagation of Requirements (guarantees to be provided by upstream components)
    Backwards propagation of “dead zone” signal range
      Results in a set of required ranges/relationships on the model inputs
      Can be used to automatically generate the Assume clause of Assume-Guarantee approach (e.g., for “No-divide-by-zero”)
  Satisfying Guarantee clauses in general
    In the PI controller proof, controller component needs to provide a guarantee that integrator term is range-limited (saturated). HiLiTE can check this.
    Many other checks that HiLiTE does (or can do) on a component that given assume clauses (ranges, temporal) certain guarantees are met.
    HiLiTE can be used to do those guarantees that are much harder to do in other tools (e.g. H-SAL, PRISM) or they would require smart user inputs. HiLiTE walks through the entire model and does certain checks without user inputs.
  Propagation of complex signal relationships
    Can be used to prove that an Assume clause is sufficient to result in a verification property
    Can be used to satisfy a Guarantee clause
      E.g., signals s1 and s2 will always be equal given a value and time delta
        The value of signal s1 may lag s2 within the time delta or vice versa
Phased Implementation Approach

## Slide 5
Component A
Certificate for Prop X
Assume: No overflows of variables v1, v2, … vn
Guarantee: Component Safety Property X
Assume-Guarantee Reasoner
If we can show:
Property X on Component A and
Property Y on Component B -->
then System-level property Z holds
HILITE
Ensure range of divide.input2 is contained in: { (MIN_INT, -0.001], [0.001, MAX_INT) }
Inport1.MinValue + Inport2.MinValue >= 0.001 AND Inport1.MaxValue + Inport2.MaxValue < MAX_INT
Backwards Propagate Range Constraints
6
5
4
3
2
1
[-10.0, 10.0]
[100.0, 999.9]
[-999.9, 999.9]
Proof: Since Inport1.MinValue + Inport2.MinValue >= 0.001 AND Inport1.MaxValue + Inport2.MaxValue < MAX_INT, --> Sum.Out != 0.0
Phase 2

## Slide 6: Summary of Integration of HiLiTE with Vanderbilt Design Tool and H-SAL
Capturing annotations in design models to enable static analysis
  (Note: New annotation are added at Meta-language level)
  Architectural models need to capture connections between inputs/outputs of component and sub-component models.
  System level information such as staleness/validity and operational ranges need to be captured for inputs coming into a “partition”
Multi-model range propagation and other analyses
  Extract annotated info from design models (plug-in into GME)
  Propagate ranges and other analyses across multiple sub-component models
    other types of analyses are described earlier
  Annotate HiLiTE results back into the design model (plug-in into GME)
  The HiLiTE results (annotated back) can be supplied to H-SAL or Maude to prune its state space.

## Slide 7: Definition of Tool Interfaces

## Slide 8
Model1
Model2
Model3
Functional Partition 1
Model1
Model2
Model3
Functional Partition 2
Model1
Model2
Model3
Functional Partition 3
Processors and Network
I/O/Msg Conversions
I/O/Msg Conversions
I/O/Msg Conversions
System Dictionaries

## Slide 9: Design Flow Analysis
Derive dependency graph by tracing through dictionary
  Check consistency against scheduling artifacts
  complexity metric
  Visualizations
Compute end-to-end transport delay – verification task
Model1
Model2
Model3
Dependency graph derivation: only show different sources (internal, extarnal) of signals

## Slide 10: System Dictionary Contents
Unique Signal Name | Data Type | Units | Physical Unit | Signal Scope | Range | Resolution | Tolerance/ Numerical Error
examples | Int32, Float64, Float32, Boolean, Uint32 | e.g., knots, degree, radian, deg C, ft, ft/min, %rpm, seconds, unitless (further defn: flag, count, ratio) | E.g., altitude, heading, roll/pitch/yaw, engine speed, air speed, | e.g: Partition Input, Intermediate, Partition Output |  | For integer: e.g., 4, 2 | For floating point variable: x% of value with a minimum for near-zero values.
Signal_A | Float32 | knots | speed |  | [0, 1000] |  | 
Signal_B | Int32 | ft | altitude |  | [0, 80000] |  | 

## Slide 11: I/O: Input and Output Transformations
A/D conversions
Packing of fields in messages on the bus
  Fixed binary standard representations (ARINC 429) of physical quantities (e.g., altitude)
  CAN-ARINC-825 (check) has similar standard representations
Impact
  – scaling: fixed point scaling – conversions need to be verified in terms of range bounds
  Resolution: coarse resolution due to message packing or A/D
    E.g., 12-bit A/D on a sensor input, D/A on an actuator
    Resolution of 4 for integer on ASCB bus
  Phase lag / delay: can degrade control
    How is sampling of the sensor value being done with respect to scheduling of control algorithm model that consumes it
      (Brian Gordon, Jay Simms, Brendan to send Jay’s email/document)
      Sensor  Bus  OS  control algorithm
      what is the maximum phase lag error and how can that degrade the control (control engineer should provide delay/phase error budget to ensure control stability)
      Note: if these are all async then the time delay error is worse than sync architecture – may require faster sampling
    What properties need to be verified on the control algorithms for sensor delay / phase lag?

## Slide 12: Design / Verification Problems to be Addressed
What constraints and design rules in the design flow (meta language)
What visualizations, design flow analysis are needed?
  Visualize dependency graph, properties on the links
  Complexity metrics: too much cross coupling among component models, too much feedback
  Simple analyses:
    only one producer of a signal
    Enumerate feedback loops

## Slide 13: Impact of Resolution on Design Correctness when Components are reused / integrated
Model1
Bus
I/O
Transform
signal_x :
integer, resolution = 4
  Example of Design Property: Automated check for numerical stability of block-level behaviors and true/false coverage on all decisions

## Slide 14: Integration with HiLiTE

## Slide 15: Using HiLiTE from a Design Flow Tool
HiLiTE
Model
Analysis
Model Summary File
(XML)
Design Property
Violations
System Dictionaries, Models
HiLiTE Command File
(XML)
Design
Tool
generate
External Input Range Files
(.csv)
Models
Intermediate Range File
(.csv)
generate
annotate
Running HiLiTE from the command line:
  % hilite command_file.hilite [args_for_command_file_if_needed]

## Slide 16: HiLiTE User Guide Readings
Getting Started with HiLiTE
A Brief HiLiTE Tutorial
Creating HiLiTE Command Files
  4.1
  4.2
  4.3.1

## Slide 17: Range File Examples

## Slide 18: Defect Reporting Examples

## Slide 19: Discussions

## Slide 20: Discussion of Relational and other Abstractions for Analyses (Ashish)
Goal: Replace certain combination of Simulink blocks (e.g., feedback loop) by others in a conservative way to enable HiLiTE to propagate ranges across them
Idea: Use a relational abstraction of a system of differential equations
  Top part of the model is described by
  dx/dt = In1 - x (Out1 == x)
  Bottom part of the model is obtained by replacing the feedback loop through the integral by a simpler loop-free block:
  Out2 = In1 * UniformRandom(0,1) where UniformRandom(0,1) returns any number between 0 and 1.
In a precise mathematical sense, the bottom part is an abstraction of the top part for computing a conservative range bound:
  Abstraction: Out2Range = In1Range X [0, 1] (X: range arithmetic operator)

## Slide 21: HiLiTE uses Range Computation Abstractions for Several Blocks
Several Simulink and flight controls library blocks are defined by z-domain transfer functions that are parameterized
For computing range bounds a priori relational abstractions for range bound computation have been created in HiLiTE from the parameterized transfer functions
  There is a long list of such blocks in flight controls
For test generation search, HiLiTE uses a different abstraction based upon difference equation derived from z-domain transfer function
  Input ↔translation during test generation is computed using the difference equation using “fixed step discrete” time semantics.
  Example for lag filter above
  Note: the block parameter is τ expressed in seconds, independent of the sampling freq
  internal constants k1, k2 are derived from τ (block parameter) and the sampling freq selected for a model
  where k1 = 2 * τ / Ts – 1 Ts: sampling time = 1 / samplingFreq
  k2 = 2 * τ / Ts + 1
    yn = (k1 * yn-1 + un + un-1) / k2
  HiLiTE solves some simple constraints in backward search (e.g., polynomials)– could use help from a constraint solver

## Slide 22: Representation of Time in Control System Models
Large avionics control system software is currently designed using discrete time semantics
  Early design and system-level simulation/validation is done using discrete time – proper sampling frequencies are used that are tuned during the design process.
  All data flow control blocks (filters, integrators): transfer functions are specified in z-domain. All parameters (e.g. Tau) are specified explicitly in seconds so that if the sampling frequency of a model is changed, it doesn’t impact the control response.
  Example: the unit of block parameter τ (Time Constant) is seconds – see dialog below:
  Practical perspective: since the flight code implementation uses periodic execution and scheduling, it is best to model the control using discrete time
    Additionally, Each model has a single periodic rate, since each model is implemented by a C-function.
Scheduling of multiple interacting models
  Each model is scheduled at its designated periodic rate
    Model’s input values are sampled at the start of each periodic execution frame, the control computations are performed, and outputs are produced that are then sampled by downstream models when those models are scheduled
    Feedback loop within a model: a unit-delay element is used in each feedback path so that the value used in the current execution frame is that produced in the previous execution frame: yn = un-1
  Input-output dependence among models
    Models are scheduled in dependence order (when on the same CPU) to minimized producer-consumer sampling delays between models – this is called “rate structured executive”
    An end-to-end (sensor to actuator) “control delay” analysis is performed on the system

## Slide 23: Hard problems are complex feedback loops involving several blocks
HiLiTE currently analyzes simple feedback loops like counters.
Ashish: Use a constraint solver to obtain relational abstraction for the range bound computation on a feedback loop
  Solvers: non-linear constraint solvers and convex optimization solvers (list in old PI mtg slides), MATLAB plug-ins as well (semi-definite programming).
  Ashish will provide analysis methodology to derive relational abstractions for feedback loop – can then be implemented in HiLiTE for discrete-time semantics
Kirk: Besides bounds, can also compute properties such as:
  range increases or decreases monotonically
  can relational abstractions be used for these types of properties?
Combination approaches: discrete stuff (e.g. reset, mode change) is interleaved with continuous dynamics in nested feedback loops
  Can we use some abstractions to conservatively simplify and then solve a simpler problem in the constraint solver and combine with the rest using abstractions?
  Relational abstractions for the feedback loops (in discrete time) still need to be derived for constraint solvers to be used.
    Hybrid and complex constraint expressions can be given to he solvers
We could layer the error propagation on top of this, so even though the blocks change, we would still retain how the representation error may change when passing through the block. (Gabor)