## Slide 1: Armor Thickness Sizing Process
Material type: Homogenous steel
Material density: 490 lb/ft^3 (from CATIA)
Abbreviations
  AP: Armor-piercing
  APIT: Armor-piercing Incendiary Tracer
Material information from MIL-STD-12560 (75-mm protection from MIL-STD-11356)
Surface area taken from baseline CATIA model hull (Design Table ACGV1101)
Material Properties |  |  |  |  |  | Vehicle Application |  | 
Minimum Thickness | Munition |  |  | Obliquity | Surface Density | Surface Area | Armor Weight | Armor Weight
(inch) | Size | Type | Weapon | Angle | (lb/ft^2) | (ft^2) | (lb) | (short ton)
0.25 | Cal .30 | AP | M2 | 0° | 10.21 | (from ProE model) | =SurfaceArea * lb/ft^2 | = Armor Weight/2000
0.565 | Cal .50 | AP | M2 | 0° | 23.07 | (from ProE model) | =SurfaceArea * lb/ft^2 | = Armor Weight/2000
1.126 | 20-mm | APIT | M602 | 0° | 45.98 | (from ProE model) | =SurfaceArea * lb/ft^2 | = Armor Weight/2000
3 | 75-mm | AP | M72 | 0° | 122.50 | (from ProE model) | =SurfaceArea * lb/ft^2 | = Armor Weight/2000
4 | 90-mm | AP | M318 | 0° | 163.33 | (from ProE model) | =SurfaceArea * lb/ft^2 | = Armor Weight/2000
Material Properties |  |  |  |  |  | Vehicle Application |  | 
Minimum Thickness | Munition |  |  | Obliquity | Surface Density | Surface Area | Armor Weight | Armor Weight
(inch) | Size | Type | Weapon | Angle | (lb/ft^2) | (ft^2) | (lb) | (short ton)
0.25 | Cal .30 | AP | M2 | 0° | 10.21 | 1330 | 13,577 | 6.79
0.565 | Cal .50 | AP | M2 | 0° | 23.07 | 1330 | 30,684 | 15.34
1.126 | 20-mm | APIT | M602 | 0° | 45.98 | 1330 | 61,151 | 30.58
3 | 75-mm | AP | M72 | 0° | 122.50 | 1330 | 162,925 | 81.46
4 | 90-mm | AP | M318 | 0° | 163.33 | 1330 | 217,233 | 108.62
Example:

## Slide 2: Armor Thickness Sizing Process
Additional protection can be added to specific areas:
Components | Protection | Width | Height | Number | Surface Area | Armor Weight | Armor Weight
 | Level | (ft) | (ft) | of Panels | (ft^2) | (lb) | (short ton)
Base protection | Level 1 | - | - | - | # | =SurfaceDensity * SurfaceArea | =Armor Weight/2000
Additional Panels 1 | Level 2 | # | # | # | =Width*Height*Num | =(SurfaceDensity Level 2-SurfaceDensity Level 1) * SurfaceArea | =Armor Weight/2000
Additional Panels 2 | Level 3 | # | # | # | =Width*Height*Num | =(SurfaceDensity Level 3-SurfaceDensity Level 1) * SurfaceArea | =Armor Weight/2000
Total | - | - | - | - | =Sum of above | =Sum of above | =Sum of above
Example:
Components | Protection | Width | Height | Number | Surface Area | Armor Weight | Armor Weight
 | Level | (ft) | (ft) | of Panels | (ft^2) | (lb) | (short ton)
Hull (base protection) | Cal .50 | - | - | - | 1330 | 30,684 | 15.34
Passenger Side Panels | 20-mm | 10 | 4 | 2 | 80 | 1,833 | 0.92
Engine Panels | 20-mm | 3 | 4 | 3 | 36 | 825 | 0.41
Total | - | - | - | - | 1446 | 33,341 | 16.67

## Slide 3: Requirements Translation
Vehicle | Stryker | LAV | AAVv2 | MPC | EFV | Namer | Bradley(M2) | Puma
Country | USA | USMC | USMC | USMC | USMC | Israel | USA | Germany
Crew | 2+9 | 3+6 | 3+25 | 3+9 | 3+17 | 3+8 | 3+7 | 3+8
Combat Weight (T) | 20 | 14.5 | 30 | 25 | 38 | 68 | 36 | 35
Specific Power (hp/T) | 18.5 | 19.5 | 17.5 | 20 | 22 | 22 | 16.7 | 30
Range (km) | 531 | 660 | 480 | 500 | 525 | 500 | 400 | 600
Max Speed (km/h) (road) | 95 | 110 | 65 | 70 | 73 | 54 | 61 | 70
Engine Power (hp) | 350 | 275 | 525 | 500 | 850 | 1,500 | 600 | 1,100
Step 1: Crew size + Protection => weight (previous slides)
Step 2: Range + Speed req. => power to weight ratio
Step 3: power to weight ratio implies minimum power
Step 4: Use DESERT to eliminate engines that do not meet the minimum power

## Slide 4: Regressions
Chart: P/W (hp/T)
| 18.5
Stryker | 531
LAV | 660
AAVv2 | 480
MPC | 500
EFV | 525
Namer | 500
Bradley(M2) | 400
Puma | 600
 | 531 | 660 | 480 | 500 | 525 | 500 | 400 | 600
Chart: P/W (hp/T)
| 18.5
Stryker | 95
LAV | 110
AAVv2 | 65
MPC | 70
EFV | 73
Namer | 54
Bradley(M2) | 61
Puma | 70
 | 95 | 110 | 65 | 70 | 73 | 54 | 61 | 70
Chart: Weight (T)
| 20
Stryker | 531
LAV | 660
AAVv2 | 480
MPC | 500
EFV | 525
Namer | 500
Bradley(M2) | 400
Puma | 600
 | 531 | 660 | 480 | 500 | 525 | 500 | 400 | 600
Chart: Weight (T)
| 20
Stryker | 95
LAV | 110
AAVv2 | 65
MPC | 70
EFV | 73
Namer | 54
Bradley(M2) | 61
Puma | 70
 | 95 | 110 | 65 | 70 | 73 | 54 | 61 | 70

## Slide 5: BACKUP SLIDES

## Slide 6
Chart: P/W (hp/T)
| 18.5
Stryker | 531
LAV | 660
AAVv2 | 480
MPC | 500
EFV | 525
Namer | 500
Bradley(M2) | 400
Puma | 600
 | 531 | 660 | 480 | 500 | 525 | 500 | 400 | 600

## Slide 7
Chart: P/W (hp/T)
| 18.5
Stryker | 95
LAV | 110
AAVv2 | 65
MPC | 70
EFV | 73
Namer | 54
Bradley(M2) | 61
Puma | 70
 | 95 | 110 | 65 | 70 | 73 | 54 | 61 | 70

## Slide 8
Chart: Weight (T)
| 20
Stryker | 531
LAV | 660
AAVv2 | 480
MPC | 500
EFV | 525
Namer | 500
Bradley(M2) | 400
Puma | 600
 | 531 | 660 | 480 | 500 | 525 | 500 | 400 | 600

## Slide 9
Chart: Weight (T)
| 20
Stryker | 95
LAV | 110
AAVv2 | 65
MPC | 70
EFV | 73
Namer | 54
Bradley(M2) | 61
Puma | 70
 | 95 | 110 | 65 | 70 | 73 | 54 | 61 | 70