## Slide 1: How to get to the Verification Problem?
Download and Install the META tools
  http://cps-vo.org/group/avm/metax/downloads
Navigate to “Documents/META Documents/Verification”
  “Verification_Models.pptx”  this PPT
  “VerificationExample.xme  GME model for the verification problem
  Generated/IFV_equ.mo  modelica representation of challenge problem
  Generated/IFV_equ.html  HTML info/documentation of the model

## Slide 2: Verification Sample Model
Purpose: Initial Integration Sandbox for Verification Tools
Approach:
Simple Components
Simple Scenario
Simple TestBench
See Embedded GME Model

## Slide 3: Simple Test Bench
Compute Acceleration
  Throttle at Max Torque (Firewalled)
  Road Scenario at static condition
  Rotational Load is Resistive and Inductive
  Drivetrain subset is Engine & Transmission Only
    Transmission Controller is simple static logic

## Slide 4: Scenario Models
Graphical Description using Control Functions
Function Behavior Specified Bilingually
  Matlab Embedded Function Subset
  Modelica Function Language

## Slide 5: Vehicle Chassis/Hull Surrogate
Input Rotational Power From DriveTrain
Input Signal Specifies Resistive Load (MR)
Internal Bond graph is a Series RL Circuit
  I is representative of vehicle mass
  MR is a modulated resistance programmable for road/incline
  Scope “Load_w” specifies a plot to generate during sim

## Slide 6: DriveTrain System
Input: Engine Throttle, Requests Torque
Diesel Engine: Produces Torque@RPM on Rotational Power Port
Transmission: Transforms Torque*RPM based on Gear Ratio. Sensors report Input/Output RPM
Transmission Controller: Uses RPM, Produces Ratio Signal
Transmission Out: Rotational Power Port

## Slide 7: Diesel Engine
Diesel Engine: Simple Engine, Source of Power
  Effort (Torque)
  Flow (w)
  Resistive Load Represents Loss in Bearings, etc.
  Scope specifies generation of plot of w during sim.
  Output on Rotational Bond Graph Port

## Slide 8: Transmission Mechanical
Simple Modulated Transformer
Senses w, computes RPM
No internal losses (for simplicity)

## Slide 9: Transmission Controller
Ultra-simple controller
  No Internal States
  Only Logic Based on Intertial State
  Modelica Syntax
  Note: Modelica Bug in Simulation
function [Ratio] = fcn(InRPM, OutRPM)#%eml
%matlab specific
#Modelica
constant Real ShiftRPM = 1800;
constant Real G1=0.235849057;
constant Real G2=0.327868852;
constant Real G3=0.431034483;
constant Real G4=0.598802395;
constant Real G5=1;
constant Real G6=1.388888889;
constant Real G1Low =0;
constant Real G1High =ShiftRPM * G1;
constant Real G2Low =G1High;
constant Real G2High =ShiftRPM * G2;
constant Real G3Low = G2High;
constant Real G3High =ShiftRPM * G3;
constant Real G4Low =G3High;
constant Real G4High =ShiftRPM * G4;
constant Real G5Low =G4High;
constant Real G5High =ShiftRPM * G5;
constant Real G6Low =G5High;
constant Real G6High =99999;
// NEED TO REMOVE "algorithm" at top
algorithm
if OutRPM < G1High then
Ratio := G1;
elseif OutRPM >= G2Low and OutRPM < G2High then
Ratio:=G2;
elseif OutRPM >= G3Low and OutRPM < G3High then
Ratio:=G3;
elseif OutRPM >= G4Low and OutRPM < G4High then
Ratio:=G4;
elseif OutRPM >= G5Low and OutRPM < G5High then
Ratio:=G5;
elseif OutRPM >= G6Low and OutRPM < G6High then
Ratio:=G6;
else
Ratio:=1;
end if;

## Slide 10: Composed System
Composition Of System
Map to Modelica Representation
  Variables Noted on Arcs and Nodes

## Slide 11: Modelica Models
Modelica Models Auto Generated
  See Embedded Link
Models and Documentation load in OpenModelica
Simulations Execute
  OM Bugs

## Slide 12: Modelica Simulation
Simulation of 25 Sec.
Effort & Flow (Torque & w) Plotted on both sides of Transmission
Work-in-Progress
  Constants Not Calibrated
  Suspect OM Bug related to if-then-else ordering

## Slide 13: To Be Done
Calibrate Model
Better Transmission Control
Resolve Simulation Bugs
Create Evaluators for Acceleration, Max Speed, Fuel Efficiency
More Scenarios
Questions/Complaints: bapty@isis.vanderbilt.edu
Kudos: lattmann@isis.vanderbilt.edu

## Slide 14: System with more state variables

## Slide 15: High level diagram
System Under Test
W 1R
W 2R
W 3R
W 4R
W 1L
W 2L
W 3L
W4L
Engine
Transmission
Transfer Case
Diff 3
Diff 4
Diff 2
Diff 1
Fuel

## Slide 16: High level test bench diagram
System Under Test
Engine
Transmission
Rotational2Translation
(wheels)
Throttle
Signal
Connection types:
Mechanical Rotational Power
Test Load
(Vehicle)
Transmission controller

## Slide 17: GME Test Bench model

## Slide 18: System Under Test Component

## Slide 19: Engine

## Slide 20: Transmission

## Slide 21: Transmission Controller

## Slide 22: Test Vehicle

## Slide 23: Flat BG
Variable name | Description
E19, e16, e8, e6 | Engine’s output torque and transmission’s input torque (Nm)
F19, f16, f15, f17, f18 | Angular velocity of engine’s output and transmission input (rad/s)
E14, e1, e13, e7, e9, e11 | Transmission’s output torque [Nm]
F14, f1, f13, f7 | Transmission’s output angular velocity [rad/s]
E2, e0, e3 | Overall ‘driving’ force on the vehicle mass [N]
F2, f0, f3, f5,f4 | Vehicle speed [m/s]
E18 | Engine’s torque source without losses [Nm], (e10 after losses, bearing loss + inertia)
(Test load MR) | Lumped parameter for all losses [Ns/m]: Road resistance + wind drag + etc.
(Test load I) | Lumped inertia value for the entire ‘vehicle’. (Mass of the vehicle [kg])

## Slide 24: Generated equations
Equations
Parameters
Initial Values
Variable definitions

## Slide 25: Modelica results
Without transmission controller
  e19: engine’s output torque
  f3: vehicle speed

## Slide 26: Simulink Results w/ Controller
Velocity
Gear Ratio
Engine RPM

## Slide 27: References
[1.] Shuvra Das: Mechatronic Modeling and Simulation Using Bond Graphs